## Slide 1: CSE 451: Operating Systems Spring 2012 Module 14 Secondary Storage
Ed Lazowska
lazowska@cs.washington.edu
Allen Center 570
Notes: 1

## Slide 2: Secondary storage
Secondary storage typically:
  is anything that is outside of “primary memory”
  does not permit direct execution of instructions or data retrieval via machine load/store instructions
Characteristics:
  it’s large: 250-2000GB
  it’s cheap: $0.05/GB for hard drives
  it’s persistent: data survives power loss
  it’s slow: milliseconds to access
    why is this slow??
  it does fail, if rarely
    big failures (drive dies; MTBF ~3 years)
      if you have 100K drives and MTBF is 3 years, that’s 1 “big failure” every 15 minutes!
    little failures (read/write errors, one byte in 1013)

## Slide 3: Another trip down memory lane …
IBM 2314
About the size of
6 refrigerators
8 x 29MB (M!)
Required similar-sized air condx!
.01% (not 1% – .01%!) the capacity of this $100 4”x6”x1” item

## Slide 4: Disk trends
Disk capacity, 1975-1989
  doubled every 3+ years
  25% improvement each year
  factor of 10 every decade
  Still exponential, but far less rapid than processor performance
Disk capacity, 1990-recently
  doubling every 12 months
  100% improvement each year
  factor of 1000 every decade
  Capacity growth 10x as fast as processor performance!

## Slide 5
Only a few years ago, we purchased disks by the megabyte (and it hurt!)
Today, 1 GB (a billion bytes) costs $1 $0.50 $0.05 from Dell (except you have to buy in increments of 40 80 250 1000 GB)
  => 1 TB costs $1K $500 $50, 1 PB costs $1M $500K $50K
Technology is amazing
  Flying a 747 6” above the ground
  Reading/writing a strip of postage stamps
But …
  Jets do crash …

## Slide 6: Memory hierarchy
Each level acts as a cache of lower levels
CPU registers
L1 cache
L2 cache
Primary Memory
Secondary Storage
Tertiary Storage
100 bytes
32KB
256KB
1GB
1TB
1PB
10 ms
1s-1hr
< 1 ns
1 ns
4 ns
60 ns

## Slide 7: Memory hierarchy: distance analogy
CPU registers
L1 cache
L2 cache
Primary Memory
Secondary Storage
Tertiary Storage
1 minute
10 minutes
1.5 hours
2 years
2,000 years
Pluto
Andromeda
“My head”
“This room”
“This building”
Olympia
seconds

## Slide 8
© 2004 Jim Gray, Microsoft Corporation

## Slide 9: Disks and the OS
Disks are messy, messy devices
  errors, bad blocks, missed seeks, etc.
Job of OS is to hide this mess from higher-level software (disk hardware increasingly helps with this)
  low-level device drivers (initiate a disk read, etc.)
  higher-level abstractions (files, databases, etc.)
OS may provide different levels of disk access to different clients
  physical disk block (surface, cylinder, sector)
  disk logical block (disk block #)
  file logical (filename, block or record or byte #)

## Slide 10: Physical disk structure
Disk components
  platters
  surfaces
  tracks
  sectors
  cylinders
  arm
  heads
platter
surface
track
sector
cylinder
arm
head

## Slide 11: Disk performance
Performance depends on a number of steps
  seek: moving the disk arm to the correct cylinder
    depends on how fast disk arm can move
      seek times aren’t diminishing very quickly (why?)
  rotation (latency): waiting for the sector to rotate under head
    depends on rotation rate of disk
      rates are increasing, but slowly (why?)
  transfer: transferring data from surface into disk controller, and from there sending it back to host
    depends on density of bytes on disk
      increasing, relatively quickly
When the OS uses the disk, it tries to minimize the cost of all of these steps
  particularly seeks and rotation

## Slide 12: Performance via disk layout
OS may increase file block size in order to reduce seeking
OS may seek to co-locate “related” items in order to reduce seeking
  blocks of the same file
  data and metadata for a file

## Slide 13: Performance via caching, pre-fetching
Keep data or metadata in memory to reduce physical disk access
  problem?
If file access is sequential, fetch blocks into memory before requested

## Slide 14: Performance via disk scheduling
Seeks are very expensive, so the OS attempts to schedule disk requests that are queued waiting for the disk
  FCFS (do nothing)
    reasonable when load is low
    long waiting time for long request queues
  SSTF (shortest seek time first)
    minimize arm movement (seek time), maximize request rate
    unfairly favors middle blocks
  SCAN (elevator algorithm)
    service requests in one direction until done, then reverse
    skews wait times non-uniformly (why?)
  C-SCAN
    like scan, but only go in one direction (typewriter)
    uniform wait times

## Slide 15: Interacting with disks
In the old days…
  OS would have to specify cylinder #, sector #, surface #, transfer size
    i.e., OS needs to know all of the disk parameters
Modern disks are even more complicated
  not all sectors are the same size, sectors are remapped, …
  disk provides a higher-level interface, e.g., SCSI
    exports data as a logical array of blocks [0 … N]
    maps logical blocks to cylinder/surface/sector
    OS only needs to name logical block #, disk maps this to cylinder/surface/sector
    on-board cache
    as a result, physical parameters are hidden from OS
      both good and bad

## Slide 16: Seagate Barracuda 3.5” disk drive
16
1Terabyte of storage (1000 GB)
$100
4 platters, 8 disk heads
63 sectors (512 bytes) per track
16,383 cylinders (tracks)
164 Gbits / inch-squared (!)
7200 RPM
300 MB/second transfer
9 ms avg. seek, 4.5 ms avg. rotational latency
1 ms track-to-track seek
32 MB cache
Notes: 16

## Slide 17: Solid state drives: imminent disruption
Hard drives are based on spinning magnetic platters
  mechanics of drives determine performance characteristics
    sector addressable, not byte addressable
    capacity improving exponentially
    sequential bandwidth improving reasonably
    random access latency improving very slowly
  cost dictated by massive economies of scale, and many decades of commercial development and optimization
17

## Slide 18
Solid state drives are based on NAND flash memory
  no moving parts; performance characteristics driven by electronics and physics – more like RAM than spinning disk
  relative technological newcomer, so costs are still quite high in comparison to hard drives, but dropping fast
18

## Slide 19: SSD performance: reads
Reads
  unit of read is a page, typically 4KB large
  today’s SSD can typically handle 10,000 – 100,000 reads/s
    0.01 – 0.1 ms read latency (50-1000x better than disk seeks)
    40-400 MB/s read throughput (1-3x better than disk seq. thpt)
19

## Slide 20: SSD performance: writes
Writes
  flash media must be erased before it can be written to
  unit of erase is a block, typically 64-256 pages long
    usually takes 1-2ms to erase a block
    blocks can only be erased a certain number of times before they become unusable – typically 10,000 – 1,000,000 times
  unit of write is a page
    writing a page can be 2-10x slower than reading a page
Writing to an SSD is complicated
  random write to existing block: read block, erase block, write back modified block
    leads to hard-drive like performance (300 random writes / s)
  sequential writes to erased blocks: fast!
    SSD-read like performance (100-200 MB/s)
20

## Slide 21: SSDs: dealing with erases, writes
Lots of higher-level strategies can help hide the warts of an SSD
  many of these work by virtualizing pages and blocks on the drive (i.e., exposing logical pages, not physical pages, to the rest of the computer)
  wear-leveling: when writing, try to spread erases out evenly across physical blocks of of the SSD
    Intel promises 100GB/day x 5 years for its SSD drives
  log-structured filesystems: convert random writes within a filesystem to log appends on the SSD (more later)
  build drives out of arrays of SSDs, add lots of cache
21

## Slide 22: SSD cost
Capacity
  today, flash SSD costs ~$2.50/GB
    1TB drive costs around $2500
      1TB hard drive costs around $50
  Data on cost trends is a little sketchy and preliminary
Energy
  SSD is typically more energy efficient than a hard drive
    1-2 watts to power an SSD
    ~10 watts to power a high performance hard drive
      (can also buy a 1 watt lower-performance drive)
22