## Slide 1: Topic
How TCP implements AIMD, part 1
  “Slow start” is a component of the AI portion of AIMD
Slow-start
Notes: CN5E slides #5-10

## Slide 2: Recall
We want TCP to follow an AIMD control law for a good allocation
Sender uses a congestion window or cwnd to set its rate (≈cwnd/RTT)
Sender uses packet loss as the network congestion signal
Need TCP to work across a very large range of rates and RTTs

## Slide 3: TCP Startup Problem
We want to quickly near the right rate, cwndIDEAL, but it varies greatly
  Fixed sliding window doesn’t adapt and is rough on the network (loss!)
  AI with small bursts adapts cwnd gently to the network, but might take a long time to become efficient

## Slide 4: Slow-Start Solution
Start by doubling cwnd every RTT
  Exponential growth (1, 2, 4, 8, 16, …)
  Start slow, quickly reach large values
AI
Fixed
Time
Window (cwnd)
Slow-start

## Slide 5: Slow-Start Solution (2)
Eventually packet loss will occur when the network is congested
  Loss timeout tells us cwnd is too large
  Next time, switch to AI beforehand
  Slowly adapt cwnd near right value
In terms of cwnd:
  Expect loss for cwndC ≈ 2BD+queue
  Use ssthresh = cwndC/2 to switch to AI

## Slide 6: Slow-Start Solution (3)
Combined behavior, after first time
  Most time spend near right value
AI
Fixed
Time
Window
ssthresh
cwndC
cwndIDEAL
AI phase
Slow-start

## Slide 7: Slow-Start (Doubling) Timeline
Increment cwnd by 1 packet for each ACK
Notes: CN5E slide #6-58

## Slide 8: Additive Increase Timeline
Increment cwnd by 1 packet every cwnd ACKs (or 1 RTT)
Notes: CN5E slides #6-59

## Slide 9: TCP Tahoe (Implementation)
Initial slow-start (doubling) phase
  Start with cwnd = 1 (or small value)
  cwnd += 1 packet per ack
Later Additive Increase phase
  cwnd += 1/cwnd packets per ack
  Roughly adds 1 packet per RTT
Switching threshold (initially infinity)
  Switch to AI when cwnd > ssthresh
  Set ssthresh = cwnd/2 after loss
  Begin with slow-start after timeout

## Slide 10: Timeout Misfortunes
Why do a slow-start after timeout?
  Instead of MD cwnd (for AIMD)
Timeouts are sufficiently long that the ack clock will have run down
  Slow-start ramps up the ack clock
We need to detect loss before a timeout to get to full AIMD
  Done in TCP Reno

## Slide 11: Topic
How TCP implements AIMD, part 2
  “Fast retransmit” and “fast recovery” are the MD portion of AIMD
AIMD sawtooth
Notes: CN5E slides #5-10

## Slide 12: Inferring Loss from ACKs
TCP uses a cumulative ACK
  Carries highest in-order seq. number
  Normally a steady advance
Duplicate ACKs give us hints about what data hasn’t arrived
  Tell us some new data did arrive, but it was not next segment
  Thus the next segment may be lost

## Slide 13: Fast Retransmit
Treat three duplicate ACKs as a loss
  Retransmit next expected segment
  Some repetition allows for reordering, but still detects loss quickly
Ack 1 2 3 4 5 5 5 5 5 5
Notes: Circle third dup ack and write “resend 6”

## Slide 14: Fast Retransmit (2)
Ack 10
Ack 11
Ack 12
Ack 13
. . .
Ack 13
Ack 13
Ack 13
Data 14
. . .
Ack 13
Ack 20
. . .
. . .
Data 20
Third duplicate ACK, so send 14
Retransmission fills in the hole at 14
ACK jumps after loss is repaired
. . .
. . .
Data 14 was lost earlier, but got 15 to 20

## Slide 15: Fast Retransmit (3)
It can repair single segment loss quickly, typically before a timeout
However, we have quiet time at the sender/receiver while waiting for the ACK to jump
And we still need to MD cwnd …

## Slide 16: Inferring Non-Loss from ACKs
Duplicate ACKs also give us hints about what data has arrived
  Each new duplicate ACK means that some new segment has arrived
  It will be the segments after the loss
  Thus advancing the sliding window will not increase the number of segments stored in the network

## Slide 17: Fast Recovery
First fast retransmit, and MD cwnd
Then pretend further duplicate ACKs are the expected ACKs
  Lets new segments be sent for ACKs
  Reconcile views when the ACK jumps
Ack 1 2 3 4 5 5 5 5 5 5
Notes: Circle third dup ack and write “resend 6”

## Slide 18: Fast Recovery (2)
Ack 12
Ack 13
Ack 13
Ack 13
Ack 13
Data 14
Ack 13
Ack 20
. . .
. . .
Data 20
Third duplicate ACK, so send 14
Data 14 was lost earlier, but got 15 to 20
Retransmission fills in the hole at 14
Set ssthresh, cwnd = cwnd/2
Data 21
Data 22
More ACKs advance window; may send segments before jump
Ack 13
Exit Fast Recovery

## Slide 19: Fast Recovery (3)
With fast retransmit, it repairs a single segment loss quickly and keeps the ack clock running
This allows us to realize AIMD
  No timeouts or slow-start after loss, just continue with a smaller cwnd
TCP Reno combines slow-start, fast retransmit and fast recovery
  Multiplicative Decrease is ½

## Slide 20: TCP Reno
MD of ½ , no slow-start
ACK clock running
TCP sawtooth
Notes: CN5E slides #6-61

## Slide 21: TCP Reno, NewReno, and SACK
Reno can repair one loss per RTT
  Multiple losses cause a timeout
NewReno further refines ACK heuristics
  Repairs multiple losses without timeout
SACK is a better idea
  Receiver sends ACK ranges so sender can retransmit without guesswork

## Slide 22: Topic
How routers can help hosts to avoid congestion
  Explicit Congestion Notification
!!
Notes: CN5E slides #5-10

## Slide 23: Congestion Avoidance vs. Control
Classic TCP drives the network into congestion and then recovers
  Needs to see loss to slow down
Would be better to use the network but avoid congestion altogether!
  Reduces loss and delay
But how can we do this?

## Slide 24: Feedback Signals
Delay and router signals can let us avoid congestion
Signal | Example Protocol | Pros / Cons
Packet loss | Classic TCP Cubic TCP (Linux) | Hard to get wrong Hear about congestion late
Packet delay | Compound TCP (Windows) | Hear about congestion early Need to infer congestion
Router indication | TCPs with Explicit Congestion Notification | Hear about congestion early Require router support

## Slide 25: ECN (Explicit Congestion Notification)
Router detects the onset of congestion via its queue
  When congested, it marks affected packets (IP header)
Notes: CN5# slides #4-34

## Slide 26: ECN (2)
Marked packets arrive at receiver; treated as loss
  TCP receiver reliably informs TCP sender of the congestion
Notes: CN5# slides #4-34

## Slide 27: ECN (3)
Advantages:
  Routers deliver clear signal to hosts
  Congestion is detected early, no loss
  No extra packets need to be sent
Disadvantages:
  Routers and hosts must be upgraded
Notes: CN5# slides #4-34