## Slide 1: Topic
The sliding window algorithm
  Pipelining and reliability
  Building on Stop-and-Wait
Yeah!
Network
Notes: CN5E slides #5-10

## Slide 2: Recall
ARQ with one message at a time is Stop-and-Wait (normal case below)
Frame 0
ACK 0
Timeout
Time
Sender
Receiver
Frame 1
ACK 1

## Slide 3: Limitation of Stop-and-Wait
It allows only a single message to be outstanding from the sender:
  Fine for LAN (only one frame fit)
  Not efficient for network paths with BD >> 1 packet

## Slide 4: Limitation of Stop-and-Wait (2)
Example: R=1 Mbps, D = 50 ms
  RTT (Round Trip Time) = 2D = 100 ms
  How many packets/sec?
  What if R=10 Mbps?

## Slide 5: Sliding Window
Generalization of stop-and-wait
  Allows W packets to be outstanding
  Can send W packets per RTT (=2D)
  Pipelining improves performance
  Need W=2BD to fill network path

## Slide 6: Sliding Window (2)
What W will use the network capacity?
Ex: R=1 Mbps, D = 50 ms
Ex: What if R=10 Mbps?

## Slide 7: Sliding Window (3)
Ex: R=1 Mbps, D = 50 ms
  2BD = 106 b/sec x 100. 10-3 sec = 100 kbit
  W = 2BD = 10 packets of 1250 bytes
Ex: What if R=10 Mbps?
  2BD = 1000 kbit
  W = 2BD = 100 packets of 1250 bytes

## Slide 8: Sliding Window Protocol
Many variations, depending on how buffers, acknowledgements, and retransmissions are handled
Go-Back-N »
  Simplest version, can be inefficient
Selective Repeat »
  More complex, better performance

## Slide 9: Sliding Window – Sender
Sender buffers up to W segments until they are acknowledged
  LFS=last frame sent, LAR=last ack rec’d
  Sends while LFS – LAR ≤ W
..
5
6
7
..
2
3
4
5
2
3
..
LAR
LFS
W=5
Acked
Unacked
3
..
Unavailable
Available
seq. number
Sliding
Window

## Slide 10: Sliding Window – Sender (2)
Transport accepts another segment of data from the Application ...
  Transport sends it (as LFS–LAR  5)
..
5
6
7
..
2
3
4
5
2
3
..
LAR
LFS
W=5
Acked
Unacked
3
..
Unavailable
seq. number
4

## Slide 11: Sliding Window – Sender (3)
Next higher ACK arrives from peer…
  Window advances, buffer is freed
  LFS–LAR  4 (can send one more)
..
5
6
7
2
3
4
5
2
3
..
LAR
LFS
W=5
Acked
3
..
Unavail.
Available
seq. number
..
2
Unacked

## Slide 12: Sliding Window – Go-Back-N
Receiver keeps only a single packet buffer for the next segment
  State variable, LAS = last ack sent
On receive:
  If seq. number is LAS+1, accept and pass it to app, update LAS, send ACK
  Otherwise discard (as out of order)

## Slide 13: Sliding Window – Selective Repeat
Receiver passes data to app in order, and buffers out-of-order segments to reduce retransmissions
ACK conveys highest in-order segment, plus hints about out-of-order segments
TCP uses a selective repeat design; we’ll see the details later

## Slide 14: Sliding Window – Selective Repeat (2)
Buffers W segments, keeps state variable, LAS = last ack sent
On receive:
  Buffer segments [LAS+1, LAS+W]
  Pass up to app in-order segments from LAS+1, and update LAS
  Send ACK for LAS regardless

## Slide 15: Sliding Window – Retransmissions
Go-Back-N sender uses a single timer to detect losses
  On timeout, resends buffered packets starting at LAR+1
Selective Repeat sender uses a timer per unacked segment to detect losses
  On timeout for segment, resend it
  Hope to resend fewer segments

## Slide 16: Sequence Numbers
Need more than 0/1 for Stop-and-Wait …
  But how many?
For Selective Repeat, need W numbers for packets, plus W for acks of earlier packets
  2W seq. numbers
  Fewer for Go-Back-N (W+1)
Typically implement seq. number with an N-bit counter that wraps around at 2N—1
  E.g., N=8: …, 253, 254, 255, 0, 1, 2, 3, …

## Slide 17: Sequence Time Plot
Time
Seq. Number
Acks
(at Receiver)
Delay (=RTT/2)
Transmissions
(at Sender)

## Slide 18: Sequence Time Plot (2)
Time
Seq. Number
Go-Back-N scenario

## Slide 19: Sequence Time Plot (3)
Time
Seq. Number
Loss
Timeout
Retransmissions

## Slide 20: Topic
Adding flow control to the sliding window algorithm
  To slow the over-enthusiastic sender
Please slow down!
Network
Notes: CN5E slides #5-10

## Slide 21: Problem
Sliding window uses pipelining to keep the network busy
  What if the receiver is overloaded?
Streaming video
Big Iron
Wee Mobile
Arg …
Notes: Icons from pixabay

## Slide 22: Sliding Window – Receiver
Consider receiver with W buffers
  LAS=last ack sent, app pulls in-order data from buffer with recv() call
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
seq. number
5
5
5
5
Acceptable
Sliding
Window

## Slide 23: Sliding Window – Receiver (2)
Suppose the next two segments arrive but app does not call recv()
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
Notes: Draw in scenario

## Slide 24: Sliding Window – Receiver (3)
Suppose the next two segments arrive but app does not call recv()
  LAS rises, but we can’t slide window!
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
Acked

## Slide 25: Sliding Window – Receiver (4)
If further segments arrive (even in order) we can fill the buffer
  Must drop segments until app recvs!
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Nothing
Acceptable
seq. number
5
5
5
5
4
4
Acked
4
4
4
Acked

## Slide 26: Sliding Window – Receiver (5)
App recv() takes two segments
  Window slides (phew)
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
4
Acked

## Slide 27: Flow Control
Avoid loss at receiver by telling sender the available buffer space
  win=#Acceptable, not W (from LAS)
..
5
6
7
5
2
3
..
LAS
W=5
Finished
3
..
Too high
Acceptable
seq. number
5
5
5
5
4
4
Acked

## Slide 28: Flow Control (2)
Sender uses the lower of the sliding window and flow control window (win) as the effective window size
..
5
6
7
5
2
3
..
LAS
WIN=3
Finished
3
..
Too high
seq. number
5
5
5
5
4
4
Acked

## Slide 29: Flow Control (3)
TCP-style example
  seq/ack sliding window
  Flow control with win
  seq + length < ack+win
  4KB buffer at receiver
  Circular buffer of bytes
Notes: CN5E slides #6-53