## Slide 1: Where we are in the Course
Moving on to the Link Layer!
Physical
Link
Network
Transport
Application

## Slide 2: Scope of the Link Layer
Concerns how to transfer messages over one or more connected links
  Messages are frames, of limited size
  Builds on the physical layer
Frame
Notes: Icon from Cisco icon library

## Slide 3: In terms of layers (2)
Actual data path
Virtual data path
Network
Link
Physical
Notes: Figure from CN5E slides #3-4

## Slide 4: Typical Implementation of Layers (2)
Notes: CN5E slides #3-22

## Slide 5: Topics
Framing
  Delimiting start/end of frames
Error detection and correction
  Handling errors
Retransmissions
  Handling loss
Multiple Access
  802.11, classic Ethernet
Switching
  Modern Ethernet
Later

## Slide 6: Topic
The Physical layer gives us a stream of bits. How do we interpret it as a sequence of frames?
…10110 …
Um?
Notes: Icons from cisco icon library

## Slide 7: Framing Methods
We’ll look at:
  Byte count (motivation)»
  Byte stuffing »
  Bit stuffing »
In practice, the physical layer often helps to identify frame boundaries
  E.g., Ethernet, 802.11

## Slide 8: Byte Count
First try:
  Let’s start each frame with a length field!
  It’s simple, and hopefully good enough …

## Slide 9: Byte Count (2)
How well do you think it works?
Notes: CN5E slides #3-7

## Slide 10: Byte Count (3)
Difficult to re-synchronize after framing error
  Want a way to scan for a start of frame
Notes: CN5E slides #3-7

## Slide 11: Byte Stuffing
Better idea:
  Have a special flag byte value that means start/end of frame
  Replace (“stuff”) the flag inside the frame with an escape code
  Complication: have to escape the escape code too!
Notes: CN5E slides #3-8

## Slide 12: Byte Stuffing (2)
Rules:
  Replace each FLAG in data with ESC FLAG
  Replace each ESC in data with ESC ESC
Notes: CN5E slides #3-8

## Slide 13: Byte Stuffing (3)
Now any unescaped FLAG is the start/end of a frame
Notes: CN5E slides #3-8

## Slide 14: Bit Stuffing
Can stuff at the bit level too
  Call a flag six consecutive 1s
  On transmit, after five 1s in the data, insert a 0
  On receive, a 0 after five 1s is deleted

## Slide 15: Bit Stuffing (2)
Example:
Transmitted bits
with stuffing
Data bits
Notes: CN5E slides #3-9

## Slide 16: Bit Stuffing (3)
So how does it compare with byte stuffing?
Transmitted bits
with stuffing
Data bits
Notes: CN5E slides #3-9

## Slide 17: Topic
Some bits will be received in error due to noise. What can we do?
  Detect errors with codes »
  Correct errors with codes »
  Retransmit lost frames
Reliability is a concern that cuts across the layers – we’ll see it again
Later
Notes: Icons from cisco icon library

## Slide 18: Problem – Noise may flip received bits
Signal
0
0
0
0
1
1
1
0
0
0
0
0
1
1
1
0
0
0
0
0
1
1
1
0
Slightly
Noisy
Very
noisy

## Slide 19: Approach – Add Redundancy
Error detection codes
  Add check bits to the message bits to let some errors be detected
Error correction codes
  Add more check bits to let some errors be corrected
Key issue is now to structure the code to detect many errors with few check bits and modest computation

## Slide 20: Motivating Example
A simple code to handle errors:
  Send two copies! Error if different.
How good is this code?
  How many errors can it detect/correct?
  How many errors will make it fail?
Notes: Draw example of coded message. 2 errors can fool it

## Slide 21: Motivating Example (2)
We want to handle more errors with less overhead
  Will look at better codes; they are applied mathematics
  But, they can’t handle all errors
  And they focus on accidental errors (will look at secure hashes later)
Notes: 2 errors can fool it -- weak

## Slide 22: Using Error Codes
Codeword consists of D data plus R check bits (=systematic block code)
Sender:
  Compute R check bits based on the D data bits; send the codeword of D+R bits
D
R=fn(D)
Data bits
Check bits

## Slide 23: Using Error Codes (2)
Receiver:
  Receive D+R bits with unknown errors
  Recompute R check bits based on the D data bits; error if R doesn’t match R’
D
R’
Data bits
Check bits
R=fn(D)
=?
Notes: Note error may be in data or check bits

## Slide 24: Intuition for Error Codes
For D data bits, R check bits:
Randomly chosen codeword is unlikely to be correct; overhead is low
All
codewords
Correct
codewords
Notes: Add size of spaces

## Slide 25: R.W. Hamming (1915-1998)
Much early work on codes:
  “Error Detecting and Error Correcting Codes”, BSTJ, 1950
See also:
  “You and Your Research”, 1986
Source: IEEE GHN, © 2009 IEEE
Notes: Source: IEEE GHN, http://www.ieeeghn.org/wiki/index.php/File:Richard_Hamming_1598.jpg, Image policy: http://www.ieeeghn.org/wiki/index.php/IEEE_GHN_image_policy

## Slide 26: Hamming Distance
Distance is the number of bit flips needed to change D1 to D2
Hamming distance of a code is the minimum distance between any pair of codewords
Notes: Use 0 -> 000 and 1 -> 111 as an example

## Slide 27: Hamming Distance (2)
Error detection:
  For a code of distance d+1, up to d errors will always be detected
Notes: Use 000, 111 code to show error detection

## Slide 28: Hamming Distance (3)
Error correction:
  For a code of distance 2d+1, up to d errors can always be corrected by mapping to the closest codeword
Notes: Use 000, 111 code to show error correction