## Slide 1
Error Coding Overview (§3.2)

## Slide 2: Topic
Some bits will be received in error due to noise. What can we do?
  Detect errors with codes »
  Correct errors with codes »
  Retransmit lost frames
Reliability is a concern that cuts across the layers – we’ll see it again
Later
Notes: Icons from cisco icon library

## Slide 3: Problem – Noise may flip received bits
Signal
0
0
0
0
1
1
1
0
0
0
0
0
1
1
1
0
0
0
0
0
1
1
1
0
Slightly
Noisy
Very
noisy

## Slide 4: Approach – Add Redundancy
Error detection codes
  Add check bits to the message bits to let some errors be detected
Error correction codes
  Add more check bits to let some errors be corrected
Key issue is now to structure the code to detect many errors with few check bits and modest computation

## Slide 5: Motivating Example
A simple code to handle errors:
  Send two copies! Error if different.
How good is this code?
  How many errors can it detect/correct?
  How many errors will make it fail?
Notes: Draw example of coded message. 2 errors can fool it

## Slide 6: Motivating Example (2)
We want to handle more errors with less overhead
  Will look at better codes; they are applied mathematics
  But, they can’t handle all errors
  And they focus on accidental errors (will look at secure hashes later)
Notes: 2 errors can fool it -- weak

## Slide 7: Using Error Codes
Codeword consists of D data plus R check bits (=systematic block code)
Sender:
  Compute R check bits based on the D data bits; send the codeword of D+R bits
D
R=fn(D)
Data bits
Check bits

## Slide 8: Using Error Codes (2)
Receiver:
  Receive D+R bits with unknown errors
  Recompute R check bits based on the D data bits; error if R doesn’t match R’
D
R’
Data bits
Check bits
R=fn(D)
=?
Notes: Note error may be in data or check bits

## Slide 9: Intuition for Error Codes
For D data bits, R check bits:
Randomly chosen codeword is unlikely to be correct; overhead is low
All
codewords
Correct
codewords
Notes: Add size of spaces

## Slide 10: R.W. Hamming (1915-1998)
Much early work on codes:
  “Error Detecting and Error Correcting Codes”, BSTJ, 1950
See also:
  “You and Your Research”, 1986
Source: IEEE GHN, © 2009 IEEE
Notes: Source: IEEE GHN, http://www.ieeeghn.org/wiki/index.php/File:Richard_Hamming_1598.jpg, Image policy: http://www.ieeeghn.org/wiki/index.php/IEEE_GHN_image_policy

## Slide 11: Hamming Distance
Distance is the number of bit flips needed to change D1 to D2
Hamming distance of a code is the minimum distance between any pair of codewords
Notes: Use 0 -> 000 and 1 -> 111 as an example

## Slide 12: Hamming Distance (2)
Error detection:
  For a code of distance d+1, up to d errors will always be detected
Notes: Use 000, 111 code to show error detection

## Slide 13: Hamming Distance (3)
Error correction:
  For a code of distance 2d+1, up to d errors can always be corrected by mapping to the closest codeword
Notes: Use 000, 111 code to show error correction

## Slide 14: Topic
Some bits may be received in error due to noise. How do we detect this?
  Parity »
  Checksums »
  CRCs »
Detection will let us fix the error, for example, by retransmission (later).
Notes: Icons from cisco icon library

## Slide 15: Simple Error Detection – Parity Bit
Take D data bits, add 1 check bit that is the sum of the D bits
  Sum is modulo 2 or XOR
Notes: Give example for 7 data bits

## Slide 16: Parity Bit (2)
How well does parity work?
  What is the distance of the code?
  How many errors will it detect/correct?
What about larger errors?
Notes: Give example for 7 data bits

## Slide 17: Checksums
Idea: sum up data in N-bit words
  Widely used in, e.g., TCP/IP/UDP
Stronger protection than parity
1500 bytes
16 bits

## Slide 18: Internet Checksum
Sum is defined in 1s complement arithmetic (must add back carries)
  And it’s the negative sum
“The checksum field is the 16 bit one's complement of the one's complement sum of all 16 bit words …” – RFC 791
Notes: Give example of 5 and -5 in 1s and 2s complement

## Slide 19: Internet Checksum (2)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d
Notes: Work through example

## Slide 20: Internet Checksum (3)
Sending:
Arrange data in 16-bit words
Put zero in checksum position, add
Add any carryover back to get 16 bits
Negate (complement) to get sum
0001
f203
f4f5
f6f7
+(0000)
------
2ddf0
ddf0
+ 2
------
ddf2
220d

## Slide 21: Internet Checksum (4)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000
Notes: Work through example

## Slide 22: Internet Checksum (5)
Receiving:
Arrange data in 16-bit words
Checksum will be non-zero, add
Add any carryover back to get 16 bits
Negate the result and check it is 0
0001
f203
f4f5
f6f7
+ 220d
------
2fffd
fffd
+ 2
------
ffff
0000

## Slide 23: Internet Checksum (6)
How well does the checksum work?
  What is the distance of the code?
  How many errors will it detect/correct?
What about larger errors?
Notes: Dist is 2, so fooled by 2 errors. But handles bursts up to 16 errors for a 16 bit checksum, and large errors ½^16

## Slide 24: Cyclic Redundancy Check (CRC)
Even stronger protection
  Given n data bits, generate k check bits such that the n+k bits are evenly divisible by a generator C
Example with numbers:
  n = 302, k = one digit, C = 3
Notes: Work though example: remainder is 2, need to add 1 to be divisible, so checksum is 1

## Slide 25: CRCs (2)
The catch:
  It’s based on mathematics of finite fields, in which “numbers” represent polynomials
  e.g, 10011010 is x7 + x4 + x3 + x1
What this means:
  We work with binary values and operate using modulo 2 arithmetic

## Slide 26: CRCs (3)
Send Procedure:
Extend the n data bits with k zeros
Divide by the generator value C
Keep remainder, ignore quotient
Adjust k check bits by remainder
Receive Procedure:
Divide and check for zero remainder

## Slide 27: CRCs (4)
Data bits:
1101011111
Check bits:
C(x)=x4+x1+1
C = 10011
k = 4
  1 0 0 1 1 1 1 0 1 0 1 1 1 1 1
Notes: Work it through …

## Slide 28: CRCs (5)
Notes: CN5E slides #3-19

## Slide 29: CRCs (6)
Protection depend on generator
  Standard CRC-32 is 10000010 01100000 10001110 110110111
Properties:
  HD=4, detects up to triple bit errors
  Also odd number of errors
  And bursts of up to k bits in error
  Not vulnerable to systematic errors like checksums

## Slide 30: Error Detection in Practice
CRCs are widely used on links
  Ethernet, 802.11, ADSL, Cable …
Checksum used in Internet
  IP, TCP, UDP … but it is weak
Parity
  Is little used