## Slide 1: Where we are in the Course
Finishing off the Link Layer!
  Builds on the physical layer to transfer frames over connected links
Physical
Link
Network
Transport
Application

## Slide 2: Topics
Framing
  Delimiting start/end of frames
Error detection/correction
  Handling errors
Done
DSL

## Slide 3: Topics (2)
Retransmissions
  Handling loss
Multiple Access
  Classic Ethernet, 802.11
Switching
  Modern Ethernet
Notes: AP from pixabay.com.
Icons from Cisco icon library

## Slide 4: Topic
Two strategies to handle errors:
Detect errors and retransmit frame (Automatic Repeat reQuest, ARQ)
Correct errors with an error correcting code
Done this
Notes: Mention: or combinations of 1 and 2

## Slide 5: Context on Reliability
Where in the stack should we place reliability functions?
Physical
Link
Network
Transport
Application

## Slide 6: Context on Reliability (2)
Everywhere! It is a key issue
  Different layers contribute differently
Physical
Link
Network
Transport
Application
Recover actions
(correctness)
Mask errors
(performance optimization)

## Slide 7: ARQ
ARQ often used when errors are common or must be corrected
  E.g., WiFi, and TCP (later)
Rules at sender and receiver:
  Receiver automatically acknowledges correct frames with an ACK
  Sender automatically resends after a timeout, until an ACK is received

## Slide 8: ARQ (2)
Normal operation (no loss)
Frame
ACK
Timeout
Time
Sender
Receiver

## Slide 9: ARQ (3)
Loss and retransmission
Frame
Timeout
Time
Sender
Receiver
Frame
ACK
X

## Slide 10: So What’s Tricky About ARQ?
Two non-trivial issues:
  How long to set the timeout? »
  How to avoid accepting duplicate frames as new frames »
Want performance in the common case and correctness always

## Slide 11: Timeouts
Timeout should be:
  Not too big (link goes idle)
  Not too small (spurious resend)
Fairly easy on a LAN
  Clear worst case, little variation
Fairly difficult over the Internet
  Much variation, no obvious bound
  We’ll revisit this with TCP (later)

## Slide 12: Duplicates
What happens if an ACK is lost?
X
Frame
ACK
Timeout
Sender
Receiver
New
Frame?
Notes: Fill in figure

## Slide 13: Duplicates (2)
What happens if an ACK is lost?
Frame
ACK
X
Frame
ACK
Timeout
Sender
Receiver
New
Frame?
New
Frame??

## Slide 14: Duplicates (3)
Or the timeout is early?
ACK
Frame
Timeout
Sender
Receiver
New
Frame?
Notes: Fill in

## Slide 15: Duplicates (4)
Or the timeout is early?
Frame
ACK
Frame
ACK
Timeout
Sender
Receiver
New
Frame?
New
Frame??

## Slide 16: Sequence Numbers
Frames and ACKs must both carry sequence numbers for correctness
To distinguish the current frame from the next one, a single bit (two numbers) is sufficient
  Called Stop-and-Wait

## Slide 17: Stop-and-Wait
In the normal case:
Time
Sender
Receiver

## Slide 18: Stop-and-Wait (2)
In the normal case:
Frame 0
ACK 0
Timeout
Time
Sender
Receiver
Frame 1
ACK 1

## Slide 19: Stop-and-Wait (3)
With ACK loss:
X
Frame 0
ACK 0
Timeout
Sender
Receiver
New
Frame?

## Slide 20: Stop-and-Wait (4)
With ACK loss:
Frame 0
ACK 0
X
Frame 0
ACK 0
Timeout
Sender
Receiver
New
Frame?
It’s a
Resend!

## Slide 21: Stop-and-Wait (5)
With early timeout:
ACK 0
Frame 0
Timeout
Sender
Receiver
New
Frame?

## Slide 22: Stop-and-Wait (6)
With early timeout:
Frame 0
ACK 0
Frame 0
ACK 0
Timeout
Sender
Receiver
New
Frame?
It’s a
Resend
OK …

## Slide 23: Limitation of Stop-and-Wait
It allows only a single frame to be outstanding from the sender:
  Good for LAN, not efficient for high BD
Ex: R=1 Mbps, D = 50 ms
  How many frames/sec? If R=10 Mbps?

## Slide 24: Sliding Window
Generalization of stop-and-wait
  Allows W frames to be outstanding
  Can send W frames per RTT (=2D)
  Various options for numbering frames/ACKs and handling loss
    Will look at along with TCP (later)

## Slide 25: Topic
Multiplexing is the network word for the sharing of a resource
Classic scenario is sharing a link among different users
  Time Division Multiplexing (TDM) »
  Frequency Division Multiplexing (FDM) »

## Slide 26: Time Division Multiplexing (TDM)
Users take turns on a fixed schedule
2
2
2
2
Notes: CN5E slides #2-38

## Slide 27: Frequency Division Multiplexing (FDM)
Put different users on different frequency bands
Overall FDM channel
Notes: CN5E slides #2-36

## Slide 28: TDM versus FDM
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 29: TDM versus FDM (2)
In TDM a user sends at a high rate a fraction of the time; in FDM, a user sends at a low rate all the time
Rate
Time
FDM
TDM

## Slide 30: TDM/FDM Usage
Statically divide a resource
  Suited for continuous traffic, fixed number of users
Widely used in telecommunications
  TV and radio stations (FDM)
  GSM (2G cellular) allocates calls using TDM within FDM

## Slide 31: Multiplexing Network Traffic
Network traffic is bursty
  ON/OFF sources
  Load varies greatly over time
Rate
Time
Rate
Time

## Slide 32: Multiplexing Network Traffic (2)
Network traffic is bursty
  Inefficient to always allocate user their ON needs with TDM/FDM
Rate
Time
Rate
Time
R
R

## Slide 33: Multiplexing Network Traffic (3)
Multiple access schemes multiplex users according to their demands – for gains of statistical multiplexing
Rate
Time
Rate
Time
Rate
Time
R
R
R’<2R
Two users, each need R
Together they need R’ < 2R

## Slide 34: Multiple Access
We will look at two kinds of multiple access protocols
Randomized. Nodes randomize their resource access attempts
  Good for low load situations
Contention-free. Nodes order their resource access attempts
  Good for high load or guaranteed quality of service situations

## Slide 35: END
© 2013 D. Wetherall
Slide material from: TANENBAUM, ANDREW S.; WETHERALL, DAVID J., COMPUTER NETWORKS, 5th Edition, © 2011. Electronically reproduced by permission of Pearson Education, Inc., Upper Saddle River, New Jersey