## Slide 1: Where we are in the Course
Beginning to work our way up starting with the Physical layer
Physical
Link
Network
Transport
Application

## Slide 2: Scope of the Physical Layer
Concerns how signals are used to transfer message bits over a link
  Wires etc. carry analog signals
  We want to send digital bits
…10110
10110…
Signal

## Slide 3: Topics
Properties of media
  Wires, fiber optics, wireless
Simple signal propagation
  Bandwidth, attenuation, noise
Modulation schemes
  Representing bits, noise
Fundamental limits
  Nyquist, Shannon

## Slide 4: Simple Link Model
We’ll end with an abstraction of a physical channel
  Rate (or bandwidth, capacity, speed) in bits/second
  Delay in seconds, related to length
Other important properties:
  Whether the channel is broadcast, and its error rate
Delay D, Rate R
Message

## Slide 5: Message Latency
Latency is the delay to send a message over a link
  Transmission delay: time to put M-bit message “on the wire”
  Propagation delay: time for bits to propagate across the wire
  Combining the two terms we have:

## Slide 6: Message Latency (2)
Latency is the delay to send a message over a link
  Transmission delay: time to put M-bit message “on the wire”
    T-delay = M (bits) / Rate (bits/sec) = M/R seconds
  Propagation delay: time for bits to propagate across the wire
    P-delay = Length / speed of signals = Length / ⅔c = D seconds
  Combining the two terms we have: L = M/R + D

## Slide 7: Metric Units
The main prefixes we use:
Use powers of 10 for rates, 2 for storage
  1 Mbps = 1,000,000 bps, 1 KB = 210 bytes
“B” is for bytes, “b” is for bits
Prefix | Exp. | prefix | exp.
K(ilo) | 103 | m(illi) | 10-3
M(ega) | 106 | μ(micro) | 10-6
G(iga) | 109 | n(ano) | 10-9
Notes: From CN5E Slides #1-42

## Slide 8: Latency Examples
“Dialup” with a telephone modem:
  D = 5 ms, R = 56 kbps, M = 1250 bytes
Broadband cross-country link:
  D = 50 ms, R = 10 Mbps, M = 1250 bytes

## Slide 9: Latency Examples (2)
“Dialup” with a telephone modem:
  D = 5 ms, R = 56 kbps, M = 1250 bytes
  L = 5 ms + (1250x8)/(56 x 103) sec = 184 ms!
Broadband cross-country link:
  D = 50 ms, R = 10 Mbps, M = 1250 bytes
  L = 50 ms + (1250x8) / (10 x 106) sec = 51 ms
A long link or a slow rate means high latency
  Often, one delay component dominates

## Slide 10: Bandwidth-Delay Product
Messages take space on the wire!
The amount of data in flight is the bandwidth-delay (BD) product
  BD = R x D
  Measure in bits, or in messages
  Small for LANs, big for “long fat” pipes

## Slide 11: Bandwidth-Delay Example
Fiber at home, cross-country
  R=40 Mbps, D=50 ms
110101000010111010101001011
Notes: AU outline, book from openclipart.org

## Slide 12: Bandwidth-Delay Example (2)
Fiber at home, cross-country
  R=40 Mbps, D=50 ms
  BD = 40 x 106 x 50 x 10-3 bits
  = 2000 Kbit
  = 250 KB
That’s quite a lot of data “in the network”!
110101000010111010101001011
Notes: AU outline, book from openclipart.org

## Slide 13: Frequency Representation
weights of harmonic frequencies
Signal over time
=
A signal over time can be represented by its frequency components (called Fourier analysis)
amplitude
Notes: Figures from CN5e slides #2-4

## Slide 14: Effect of Less Bandwidth
Lost!
Fewer frequencies (=less bandwidth) degrades signal
Lost!
14
Lost!
Bandwidth
Notes: Ask which signal we’d like to get out? (middle) Figures from CN5e slides #2-4

## Slide 15: Signals over a Wire
What happens to a signal as it passes over a wire?
  The signal is delayed (propagates at ⅔c)
  The signal is attenuated (goes for m to km)
  Frequencies above a cutoff are highly attenuated
  Noise is added to the signal (later, causes errors)
EE: Bandwidth = width of frequency band, measured in Hz
CS: Bandwidth = information carrying capacity, in bits/sec
Notes: Write c = speed of light

## Slide 16: Signals over a Wire (2)
Example:
2: Attenuation:
3: Bandwidth:
4: Noise:
Sent signal

## Slide 17: Signals over Fiber
Light propagates with very low loss in three very wide frequency bands
  Use a carrier to send information
Wavelength (μm)
Attenuation
(dB/km
By SVG: Sassospicco Raster: Alexwind, CC-BY-SA-3.0, via Wikimedia Commons

## Slide 18: Signals over Wireless
Signals transmitted on a carrier frequency, like fiber (more later)

## Slide 19: Signals over Wireless (2)
Travel at speed of light, spread out and attenuate faster than 1/dist2
Signal
strength
Distance
A
B

## Slide 20: Signals over Wireless (3)
Multiple signals on the same frequency interfere at a receiver
Signal
strength
Distance
A
B
C
Notes: Write what C sees

## Slide 21: Signals over Wireless (4)
Interference leads to notion of spatial reuse (of same freq.)
Signal
strength
Distance
A
B
C

## Slide 22: Signals over Wireless (5)
Various other effects too!
  Wireless propagation is complex, depends on environment
Some key effects are highly frequency dependent,
  E.g., multipath at microwave frequencies

## Slide 23: Wireless Multipath
Signals bounce off objects and take multiple paths
  Some frequencies attenuated at receiver, varies with location
  Messes up signal; handled with sophisticated methods (§2.5.3)
Notes: CN5E slides #2-23. Show constructive / destructive interference

## Slide 24: Wireless
Sender radiates signal over a region
  In many directions, unlike a wire, to potentially many receivers
  Nearby signals (same freq.) interfere at a receiver; need to coordinate use
Notes: Radio icon from openclipart.org, laptop icon from Cisco icon library

## Slide 25
WiFi
WiFi
Notes: Chart from http://www.ntia.doc.gov/page/2011/united-states-frequency-allocation-chart, public domain

## Slide 26: Wireless (2)
Microwave, e.g., 3G, and unlicensed (ISM) frequencies, e.g., WiFi, are widely used for computer networking
802.11
b/g/n
802.11a/g/n
Notes: Figure from CN5E slide #2-20

## Slide 27: Topic
We’ve talked about signals representing bits. How, exactly?
  This is the topic of modulation
…10110
10110…
Signal
Notes: Laptop from Cisco Icon library

## Slide 28: A Simple Modulation
Let a high voltage (+V) represent a 1, and low voltage (-V) represent a 0
  This is called NRZ (Non-Return to Zero)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
+V
-V

## Slide 29: A Simple Modulation (2)
Let a high voltage (+V) represent a 1, and low voltage (-V) represent a 0
  This is called NRZ (Non-Return to Zero)
Bits
NRZ
0
0
1
0
1
1
1
1
0
1
0
0
0
0
1
0
+V
-V

## Slide 30: Many Other Schemes
Can use more signal levels, e.g., 4 levels is 2 bits per symbol
Practical schemes are driven by engineering considerations
  E.g., clock recovery »
Notes: Draw in a 4-level signal next to a 2-level one

## Slide 31: Clock Recovery
Um, how many zeros was that?
  Receiver needs frequent signal transitions to decode bits
Several possible designs
  E.g., Manchester coding and scrambling (§2.5.1)
1 0 0 0 0 0 0 0 0 0 … 0

## Slide 32: Clock Recovery – 4B/5B
Map every 4 data bits into 5 code bits without long runs of zeros
  0000  11110, 0001  01001, 1110  11100, … 1111  11101
  Has at most 3 zeros in a row
  Also invert signal level on a 1 to break up long runs of 1s (called NRZI, §2.5.1)

## Slide 33: Clock Recovery – 4B/5B (2)
4B/5B code for reference:
  000011110, 000101001, 111011100, … 111111101
Message bits: 1 1 1 1 0 0 0 0 0 0 0 1
Coded Bits:
Signal:

## Slide 34: Clock Recovery – 4B/5B (3)
4B/5B code for reference:
  000011110, 000101001, 111011100, … 111111101
Message bits: 1 1 1 1 0 0 0 0 0 0 0 1
Coded Bits:
Signal:
1 1 1 0 1 1 1 1 1 0 0 1 0 0 1

## Slide 35: Passband Modulation
What we have seen so far is baseband modulation for wires
  Signal is sent directly on a wire
These signals do not propagate well on fiber / wireless
  Need to send at higher frequencies
Passband modulation carries a signal by modulating a carrier

## Slide 36: Passband Modulation (2)
Carrier is simply a signal oscillating at a desired frequency:
We can modulate it by changing:
  Amplitude, frequency, or phase

## Slide 37: Passband Modulation (3)
NRZ signal of bits
Amplitude shift keying
Frequency shift keying
Phase shift keying
Notes: Figure derived from CN5E figures #2-23. Write “baseband” under NRZ.

## Slide 38: Topic
How rapidly can we send information over a link?
  Nyquist limit (~1924) »
  Shannon capacity (1948) »
Practical systems are devised to approach these limits

## Slide 39: Key Channel Properties
The bandwidth (B), signal strength (S), and noise strength (N)
  B limits the rate of transitions
  S and N limit how many signal levels we can distinguish
Bandwidth B
Signal S,
Noise N

## Slide 40: Nyquist Limit
The maximum symbol rate is 2B
Thus if there are V signal levels, ignoring noise, the maximum bit rate is:
R = 2B log2V bits/sec
1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1 0 1

## Slide 41: Claude Shannon (1916-2001)
Father of information theory
  “A Mathematical Theory of Communication”, 1948
Fundamental contributions to digital computers, security, and communications
Credit: Courtesy MIT Museum
Electromechanical mouse that “solves” mazes!
Notes: Hi, This photo is negative number CES 7 in our collection. We allow free use of our images at 72dpi and under 730px/side for educational purposes, as long as proper credit is given; if the image below is suitable for your needs, please use it with the credit line "Courtesy MIT Museum". http://webmuseum.mit.edu/images/DIAmed/C/CES_7.jpg Additional photos of Claude Shannon in our collection may be viewed here: http://webmuseum.mit.edu/detail.php?t=people&type=all&f=&s=shannon&record=2 and more information on the maze being demonstrated in the photo is available here: http://museum.mit.edu/150/20 Please let me know if there's anything else I can do to help! Best regards, Ariel Weinberg Curatorial Associate, Science & Technology Collections MIT Museum, Building N52 265 Massachusetts Avenue Cambridge MA 02139-4307 tel: 617-253-3378 fax: 617-253-8994 http://web.mit.edu/museum On Jan 10, 2013, at 12:21 PM, Mary Anne Hansen wrote: > Hello Professor, > > The image in question does not belong to the News Office. > > By way of this email, I am forwarding your request to my colleague Ariel Weinberg, > Curatorial Associate at the MIT Museum who may be able to assist you. > > Best regards, > Mary Anne Hansen > Senior Administrative Assistant > MIT News Office, 11-400 > 617-253-8608 > > From: David Wetherall <djw@cs.washington.edu> > Date: Thursday, January 10, 2013 11:48 AM > To: "newsoffice@MIT.EDU" <newsoffice@MIT.EDU> > Subject: permissions request > > Hi, > > I am a professor teaching a massive free online course on Coursera (https://www.coursera.org/course/comnetworks). I came across your article on the Shannon limit: > > http://web.mit.edu/newsoffice/2010/explained-shannon-0115.html > > I'm asking for permission to reuse the photo in my videos and slides, which will be posted online. > > Please let me know how to proceed. > > Thank you, > > David

## Slide 42: Shannon Capacity
How many levels we can distinguish depends on S/N
  Or SNR, the Signal-to-Noise Ratio
  Note noise is random, hence some errors
SNR given on a log-scale in deciBels:
  SNRdB = 10log10(S/N)
0
1
2
3
N
S+N
Notes: Go over examples

## Slide 43: Shannon Capacity (2)
Shannon limit is for capacity (C), the maximum information carrying rate of the channel:
C = B log2(1 + S/N) bits/sec

## Slide 44: Wired/Wireless Perspective
Wires, and Fiber
  Engineer link to have requisite SNR and B
  Can fix data rate
Wireless
  Given B, but SNR varies greatly, e.g., up to 60 dB!
  Can’t design for worst case, must adapt data rate

## Slide 45: Wired/Wireless Perspective (2)
Wires, and Fiber
  Engineer link to have requisite SNR and B
  Can fix data rate
Wireless
  Given B, but SNR varies greatly, e.g., up to 60 dB!
  Can’t design for worst case, must adapt data rate
Engineer SNR for data rate
Adapt data rate to SNR

## Slide 46: Putting it all together – DSL
DSL (Digital Subscriber Line, see §2.6.3) is widely used for broadband; many variants offer 10s of Mbps
  Reuses twisted pair telephone line to the home; it has up to ~2 MHz of bandwidth but uses only the lowest ~4 kHz
Notes: Draw lines to home, say rate depends on dist/quality
Home from openclipart.org, building from cisco icon library.

## Slide 47: DSL (2)
DSL uses passband modulation (called OFDM §2.5.1)
  Separate bands for upstream and downstream (larger)
  Modulation varies both amplitude and phase (called QAM)
  High SNR, up to 15 bits/symbol, low SNR only 1 bit/symbol
Upstream
Downstream
26 – 138
kHz
0-4
kHz
143 kHz to 1.1 MHz
Telephone
Freq.
Voice
Up to 1 Mbps
Up to 12 Mbps
ADSL2: