## Slide 1: EL-E: Assistive Mobile Manipulator
David Lattanzi
Dept. of Civil and Environmental Engineering

## Slide 2: System Overview
Constructed circa 2009 at Georgia Tech
Goal: fetch and place random objects in random environments
Aid those with motor impairments (ALS)
Directions given via laser pointer

## Slide 3: Robot Design
5-DOF manipulator
Vertical actuator
Gripper
Wheeled base
Security sensors:
  Laser range finder
  Pressure plate

## Slide 4: Hardware Cont’d
On board Mac Mini
  Simpler than HERB 2.0
Omni-cam for laser pointer detection
Stereo camera for object recognition

## Slide 5: “Pick and Place” Concept
Detect laser pointer
Coarse motion
Find surface
Midscale motion

## Slide 6: “Pick and Place” Concept
Collision/grasp check
Segment objects
Pick up/drop object

## Slide 7: Coarse Scale Navigation
Use laser target to set goal
“ego-centric”, works in arbitrary environment
Gets within 0.5m
Moves linearly
  …no map
  …no planning?

## Slide 8: Surface Segmentation
Focused ROI
Uses height histogram
3D point clouds
Assumes flat surface
Determines height

## Slide 9: Midscale Navigation
Get within segmentation range
Get object into ROI
Approach normal to surface
Ends 40cm from edge
  10 cm difference?

## Slide 10: Object Segmentation
Remove points below surface
No prebuilt object models
Connected component analysis
Removes “noise”…limits resolution

## Slide 11: Fine Scale Navigation
Get within manipulator range
Picks object closest to laser target
If no object in segmentation, move and rescan
Safety scanning is on-going

## Slide 12: Grasping
Check for collisions
Find axis of minimum variance
Pick from overhead
Force sensors in gripper verify pick

## Slide 13: Placement
Basically grasping in reverse
10 cm range from edge of table
Place from overhead
Force sensors in gripper verify placement

## Slide 14: Safety and Error Monitoring
Verifies flat surface for pick and place
Checks for obstacles in path
Collision detection
  Force plate
  In ROI
Rudimentary vs. HERB

## Slide 15: System Testing
Notes: Tested on different surfaces and different objects

## Slide 16: Failures
Segmentation Failures:
  Reflective objects don’t scan properly
  Flat objects can’t be segmented from surface
  Cluttered objects fail during connected components
  Small objects removed during de-noising
Grasping Failures:
  Objects too large for gripper
  Can’t detect thin object in grasp

## Slide 17: Conclusions
Less sophisticated than HERB
  Less of a multi-purpose tool
Works without maps and models
  Lower dimensional demands
Only as good as the segmentation methods
Expansions for the future:
  Grasping from horizontal (take book off of shelf)
  Smart about object orientation (hot coffee, etc)