## Slide 1: The Hardware/Software Interface CSE351 Spring 2011 1st Lecture, March 28
Instructor:
Luis Ceze
Teaching Assistants:
Aaron Miller, David Cohen

## Slide 2: Who is Luis?
PhD in architecture,
multiprocessors, parallelism,
compilers.

## Slide 3: Who are you?
55+ students (wow!)
Who has written programs in assembly before?
Written a threaded program before?
What is an interface?
Why do we need a hardware/software interface?

## Slide 4: C vs. Assembler vs. Machine Programs
The three program fragments are equivalent
You'd rather write C!
The hardware likes bit strings!
  The machine instructions are actually much shorter than the bits required torepresent the characters of the assembler code
if ( x != 0 ) y = (y+z) / x;
cmpl $0, -4(%ebp)
je .L2
movl -12(%ebp), %eax
movl -8(%ebp), %edx
leal (%edx,%eax), %eax
movl %eax, %edx
sarl $31, %edx
idivl -4(%ebp)
movl %eax, -8(%ebp)
.L2:
1000001101111100001001000001110000000000
0111010000011000
10001011010001000010010000010100
10001011010001100010010100010100
100011010000010000000010
1000100111000010
110000011111101000011111
11110111011111000010010000011100
10001001010001000010010000011000

## Slide 5: HW/SW Interface: The Historical Perspective
Hardware started out quite primitive
  Design was expensive  the instruction set was very simple
    E.g., a single instruction can add two integers
Software was also very primitive
Hardware
Architecture Specification (Interface)

## Slide 6: HW/SW Interface: Assemblers
Life was made a lot better by assemblers
  1 assembly instruction = 1 machine instruction, but...
  different syntax: assembly instructions are character strings, not bit strings
Hardware
User Program in Asm
Assembler specification
Assembler

## Slide 7: HW/SW Interface: Higher Level Languages (HLL's)
Higher level of abstraction:
  1 HLL line is compiled into many (many) assembler lines
Hardware
User Program in C
C language specification
Assembler
C
Compiler

## Slide 8: HW/SW Interface: Code / Compile / Run Times
Hardware
User Program in C
Assembler
C
Compiler
.exe File
Code Time
Compile Time
Run Time
Note: The compiler and assembler are just programs, developed using this same process.

## Slide 9: Overview
Course themes: big and little
Four important realities
How the course fits into the CSE curriculum
Logistics
(ready? )

## Slide 10: The Big Theme
THE HARDWARE/SOFTWARE INTERFACE
How does the hardware (0s and 1s, processor executing instructions) relate to the software (Java programs)?
Computing is about abstractions (but don’t forget reality)
What are the abstractions that we use?
What do YOU need to know about them?
  When do they break down and you have to peek under the hood?
  What assumptions are being made that may or may not hold in a new context or for a new technology?
  What bugs can they cause and how do you find them?
Become a better programmer and begin to understand the thought processes that go into building computer systems

## Slide 11: Little Theme 1: Representation
All digital systems represent everything as 0s and 1s
Everything includes:
  Numbers – integers and floating point
  Characters – the building blocks of strings
  Instructions – the directives to the CPU that make up a program
  Pointers – addresses of data objects in memory
These encodings are stored in registers, caches, memories, disks, etc.
They all need addresses
  A way to find them
  Find a new place to put a new item
  Reclaim the place in memory when data no longer needed

## Slide 12: Little Theme 2: Translation
There is a big gap between how we think about programs and data and the 0s and 1s of computers
Need languages to describe what we mean
Languages need to be translated one step at a time
  Word-by-word
  Phrase structures
  Grammar
We know Java as a programming language
  Have to work our way down to the 0s and 1s of computers
  Try not to lose anything in translation!
  We’ll encounter Java byte-codes, C language, assembly language, and machine code (for the X86 family of CPU architectures)

## Slide 13: Little Theme 3: Control Flow
How do computers orchestrate the many things they are doing – seemingly in parallel
What do we have to keep track of when we call a method, and then another, and then another, and so on
How do we know what to do upon “return”
User programs and operating systems
  Multiple user programs
  Operating system has to orchestrate them all
    Each gets a share of computing cycles
    They may need to share system resources (memory, I/O, disks)
  Yielding and taking control of the processor
    Voluntary or by force?

## Slide 14: Course Outcomes
Foundation: basics of high-level programming (Java)
Understanding of some of the abstractions that exist between programs and the hardware they run on, why they exist, and how they build upon each other
Knowledge of some of the details of underlying implementations
Become more effective programmers
  More efficient at finding and eliminating bugs
  Understand the many factors that influence program performance
  Facility with some of the many languages that we use to describe programs and data
Prepare for later classes in CSE

## Slide 15: Reality 1: Ints ≠ Integers & Floats ≠ Reals
Representations are finite
Example 1: Is x2 ≥ 0?
  Floats: Yes!
  Ints:
    40000 * 40000 --> 1600000000
    50000 * 50000 --> ??
Example 2: Is (x + y) + z = x + (y + z)?
  Unsigned & Signed Ints: Yes!
  Floats:
    (1e20 + -1e20) + 3.14 --> 3.14
    1e20 + (-1e20 + 3.14) --> ??

## Slide 16: Code Security Example
Similar to code found in FreeBSD’s implementation of getpeername
There are legions of smart people trying to find vulnerabilities in programs
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE]; int len = KSIZE;
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
if (KSIZE > maxlen) len = maxlen;
memcpy(user_dest, kbuf, len);
return len;
}

## Slide 17: Typical Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE]; int len = KSIZE;
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
if (KSIZE > maxlen) len = maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, MSIZE);
printf(“%s\n”, mybuf);
}

## Slide 18: Malicious Usage
/* Kernel memory region holding user-accessible data */
#define KSIZE 1024
char kbuf[KSIZE]; int len = KSIZE;
/* Copy at most maxlen bytes from kernel region to user buffer */
int copy_from_kernel(void *user_dest, int maxlen) {
/* Byte count len is minimum of buffer size and maxlen */
if (KSIZE > maxlen) len = maxlen;
memcpy(user_dest, kbuf, len);
return len;
}
#define MSIZE 528
void getstuff() {
char mybuf[MSIZE];
copy_from_kernel(mybuf, -MSIZE);
. . .
}

## Slide 19: Reality #2: You’ve Got to Know Assembly
Chances are, you’ll never write a program in assembly code
  Compilers are much better and more patient than you are
But: Understanding assembly is the key to the machine-level execution model
  Behavior of programs in presence of bugs
    High-level language model breaks down
  Tuning program performance
    Understand optimizations done/not done by the compiler
    Understanding sources of program inefficiency
  Implementing system software
    Operating systems must manage process state
  Creating / fighting malware
  x86 assembly is the language of choice

## Slide 20: Assembly Code Example
Time Stamp Counter
  Special 64-bit register in Intel-compatible machines
  Incremented every clock cycle
  Read with rdtsc instruction
Application
  Measure time (in clock cycles) required by procedure
  double t;
  start_counter();
  P();
  t = get_counter();
  printf("P required %f clock cycles\n", t);

## Slide 21: Code to Read Counter
Write small amount of assembly code using GCC’s asm facility
Inserts assembly code into machine code generated by compiler
/* Set *hi and *lo to the high and low order bits
of the cycle counter.
*/
void access_counter(unsigned *hi, unsigned *lo)
{
asm("rdtsc; movl %%edx,%0; movl %%eax,%1"
: "=r" (*hi), "=r" (*lo) /* output */
: /* input */
: "%edx", "%eax"); /* clobbered */
}

## Slide 22: Reality #3: Memory Matters
Memory is not unbounded
  It must be allocated and managed
  Many applications are memory-dominated
Memory referencing bugs are especially pernicious
  Effects are distant in both time and space
Memory performance is not uniform
  Cache and virtual memory effects can greatly affect program performance
  Adapting program to characteristics of memory system can lead to major speed improvements

## Slide 23: Memory Referencing Bug Example
double fun(int i)
{
volatile double d[1] = {3.14};
volatile long int a[2];
a[i] = 1073741824; /* Possibly out of bounds */
return d[0];
}
fun(0) –> 3.14
fun(1) –> 3.14
fun(2) –> 3.1399998664856
fun(3) –> 2.00000061035156
fun(4) –> 3.14, then segmentation fault

## Slide 24: Memory Referencing Bug Example
double fun(int i)
{
volatile double d[1] = {3.14};
volatile long int a[2];
a[i] = 1073741824; /* Possibly out of bounds */
return d[0];
}
fun(0) –> 3.14
fun(1) –> 3.14
fun(2) –> 3.1399998664856
fun(3) –> 2.00000061035156
fun(4) –> 3.14, then segmentation fault
Saved State
d7 … d4
d3 … d0
a[1]
a[0]
0
1
2
3
4
Location accessed by fun(i)
Explanation:

## Slide 25: Memory Referencing Errors
C (and C++) do not provide any memory protection
  Out of bounds array references
  Invalid pointer values
  Abuses of malloc/free
Can lead to nasty bugs
  Whether or not bug has any effect depends on system and compiler
  Action at a distance
    Corrupted object logically unrelated to one being accessed
    Effect of bug may be first observed long after it is generated
How can I deal with this?
  Program in Java (or C#, or ML, or …)
  Understand what possible interactions may occur
  Use or develop tools to detect referencing errors

## Slide 26: Memory System Performance Example
Hierarchical memory organization
Performance depends on access patterns
  Including how program steps through multi-dimensional array
void copyji(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (j = 0; j < 2048; j++)
for (i = 0; i < 2048; i++)
dst[i][j] = src[i][j];
}
void copyij(int src[2048][2048],
int dst[2048][2048])
{
int i,j;
for (i = 0; i < 2048; i++)
for (j = 0; j < 2048; j++)
dst[i][j] = src[i][j];
}
21 times slower (Pentium 4)

## Slide 27: The Memory Mountain
s1
s3
s5
s7
s9
s11
s13
s15
8m
2m
512k
128k
32k
8k
2k
0
200
400
600
800
1000
1200
Read throughput (MB/s)
Stride (words)
Working set size (bytes)
Pentium III Xeon
550 MHz
16 KB on-chip L1 d-cache
16 KB on-chip L1 i-cache
512 KB off-chip unified
L2 cache
L1
L2
Mem

## Slide 28: Reality #4: Performance isn’t counting ops
Exact op count does not predict performance
  Easily see 10:1 performance range depending on how code written
  Must optimize at multiple levels: algorithm, data representations, procedures, and loops
Must understand system to optimize performance
  How programs compiled and executed
  How memory system is organized
  How to measure program performance and identify bottlenecks
  How to improve performance without destroying code modularity and generality

## Slide 29: Example Matrix Multiplication
Standard desktop computer, vendor compiler, using optimization flags
Both implementations have exactly the same operations count (2n3)
160x
Triple loop
Best code (K. Goto)

## Slide 30: MMM Plot: Analysis
Memory hierarchy and other optimizations: 20x
Vector instructions: 4x
Multiple threads: 4x
Reason for 20x: blocking or tiling, loop unrolling, array scalarization, instruction scheduling, search to find best choice
Effect: less register spills, less L1/L2 cache misses, less TLB misses

## Slide 31: CSE351’s role in new CSE Curriculum
Pre-requisites
  142 and 143: Intro Programming I and II
One of 6 core courses
  311: Foundations I
  312: Foundations II
  331: SW Design and Implementation
  332: Data Abstractions
  351: HW/SW Interface
  352: HW Design and Implementation
351 sets the context for many follow-on courses

## Slide 32: CSE351’s place in new CSE Curriculum
CSE351
CSE451
Op Systems
CSE401
Compilers
Concurrency
CSE333
Systems Prog
Performance
CSE484
Security
CSE466
Emb Systems
CS 143
Intro Prog II
CSE352
HW Design
Comp. Arch.
CSE461
Networks
Machine
Code
Distributed Systems
CSE477/481
Capstones
  The HW/SW Interface Underlying principles linking hardware and software
Execution Model
Real-Time Control

## Slide 33: Course Perspective
Most systems courses are Builder-Centric
  Computer Architecture
    Design pipelined processor in Verilog
  Operating Systems
    Implement large portions of operating system
  Compilers
    Write compiler for simple language
  Networking
    Implement and simulate network protocols

## Slide 34: Course Perspective (Cont.)
This course is Programmer-Centric
  Purpose is to show how software really works
  By understanding the underlying system, one can be more effective as a programmer
    Better debugging
    Better basis for evaluating performance
    How multiple activities work in concert (e.g., OS and user programs)
  Not just a course for dedicated hackers
    What every CSE major needs to know
  Provide a context in which to place the other CSE courses you’ll take

## Slide 35: Textbooks
Computer Systems: A Programmer’s Perspective, 2nd Edition
  Randal E. Bryant and David R. O’Hallaron
  Prentice-Hall, 2010
  http://csapp.cs.cmu.edu
  This book really matters for the course!
    How to solve labs
    Practice problems typical of exam problems
A good C book.
  C: A Reference Manual (Harbison and Steele)
  The C Programming Language (Kernighan and Ritchie)

## Slide 36: Course Components
Lectures (~30)
  Higher-level concepts – I’ll assume you’ve done the reading in the text
Sections (~10)
  Applied concepts, important tools and skills for labs, clarification of lectures, exam review and preparation
Written assignments (4)
  Problems from text to solidify understanding
Labs (4)
  Provide in-depth understanding (via practice) of an aspect of systems
Exams (midterm + final)
  Test your understanding of concepts and principles

## Slide 37: Resources
Course Web Page
  http://www.cse.washington.edu/351
  Copies of lectures, assignments, exams
Course Discussion Board
  Keep in touch outside of class – help each other
  Staff will monitor and contribute
Course Mailing List
  Low traffic – mostly announcements; you are already subscribed
Staff email
  Things that are not appropriate for discussion board or better offline
Anonymous Feedback (will be linked from homepage)
  Any comments about anything related to the course where you would feel better not attaching your name

## Slide 38: Policies: Grading
Exams: weighted 1/3 (midterm), 2/3 (final)
Written assignments: weighted according to effort
  We’ll try to make these about the same
Labs assignments: weighted according to effort
  These will likely increase in weight as the quarter progresses
Grading:
  25% written assignments
  35% lab assignments
  40% exams

## Slide 39: Welcome to CSE351!
Let’s have fun
Let’s learn – together
Let’s communicate
Let’s set the bar for a useful and interesting class
Many thanks to the many instructors who have shared their lecture notes – I will be borrowing liberally through the qtr – they deserve all the credit, the errors are all mine
  UW: Gaetano Borriello (Inaugural edition of CSE 351, Spring 2010)
  CMU: Randy Bryant, David O’Halloran, Gregory Kesden, Markus Püschel
  Harvard: Matt Welsh
  UW: Tom Anderson, Luis Ceze, John Zahorjan