## Slide 1: CSE351
Announcements:
  HW0, having fun?
  Use discussion boards!
  Sign up for cse351@cs mailing list
    If you enrolled recently, you might not be on it

## Slide 2: Today’s topics
Memory and its bits, bytes, and integers
Representing information as bits
Bit-level manipulations
  Boolean algebra
  Boolean algebra in C

## Slide 3: Hardware: Logical View
CPU
Memory
Bus
Disks
Net
USB
Etc.

## Slide 4: Hardware: Semi-Logical View

## Slide 5: Hardware: Physical View

## Slide 6: Performance: It's Not Just CPU Speed
Data and instructions reside in memory
  To execute an instruction, it must be fetched onto the CPU
  Then, the data the instruction operates on must be fetched onto the CPU
CPU  Memory bandwidth can limit performance
  Improving performance 1: hardware improvements to increase memory bandwidth (e.g., DDR → DDR2 → DDR3)
  Improving performance 2: move less data into/out of the CPU
    Put some “memory” on the CPU chip
    The next slide is just an introduction. We'll see a more full explanation later in the course.

## Slide 7: CPU “Memory”: Registers and Instruction Cache
There are a fixed number of registers on the CPU
  Registers hold data
There is an I-cache on the CPU holding recently fetched instructions
  If you execute a loop that fits in the cache, the CPU goes to memory for those instructions only once, then executes out of its cache
Instruction Cache
Registers
Memory
Program controlled data movement
Transparent (hw controlled) instruction caching
CPU

## Slide 8
Introduction to Memory

## Slide 9: Binary Representations
Base 2 number representation
  Represent 35110 as 00000001010111112 or 1010111112
Electronic implementation
  Easy to store with bi-stable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.5V
2.8V
3.3V
0
1
0

## Slide 10: Encoding Byte Values
Binary 000000002 -- 111111112
  Byte = 8 bits (binary digits)
Decimal 010 -- 25510
Hexadecimal 0016 -- FF16
  Byte = 2 hexadecimal (hex) or base 16 digits
  Base-16 number representation
  Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
  Write FA1D37B16 in C
    as 0xFA1D37B or 0xfa1d37b
0
0
0000
1
1
0001
2
2
0010
3
3
0011
4
4
0100
5
5
0101
6
6
0110
7
7
0111
8
8
1000
9
9
1001
A
10
1010
B
11
1011
C
12
1100
D
13
1101
E
14
1110
F
15
1111
Hex
Decimal
Binary

## Slide 11: What is memory, really?
How do we find data in memory?

## Slide 12: Byte-Oriented Memory Organization
Programs refer to addresses
  Conceptually, a very large array of bytes
  System provides an address space private to each “process”
    Process = program being executed + its data + its “state”
    Program can clobber its own data, but not that of others
    Clobbering code or “state” often leads to crashes (or security holes)
Compiler + run-time system control memory allocation
  Where different program objects should be stored
  All allocation within a single address space
• • •
00•••0
FF•••F

## Slide 13: Machine Words
Machine has a “word size”
  Nominal size of integer-valued data
    Including addresses
  Most current machines use 32 bits (4 bytes) words
    Limits addresses to 4GB
    Becoming too small for memory-intensive applications
  High-end systems use 64 bits (8 bytes) words
    Potential address space  1.8 X 1019 bytes
    x86-64 machines support 48-bit addresses: 256 Terabytes
    Can’t be real physical addresses -> virtual addresses
  Machines support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 14: Word-Oriented Memory Organization
Addresses specify locations of bytes in memory
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
  Address of word 0, 1, .. 10?
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 15: Addresses and Pointers
Address is a location in memory
Pointer is a data object that contains an address
Address 0004 stores the value 351 (or 15F16)
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
5F
01
00
00

## Slide 16: Addresses and Pointers
Address is a location in memory
Pointer is a data object that contains an address
Address 0004 stores the value 351 (or 15F16)
Pointer to address 0004 stored at address 001C
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
04
00
00
00
5F
01
00
00

## Slide 17: Addresses and Pointers
Address is a location in memory
Pointer is a data object that contains an address
Address 0004 stores the value 351 (or 15F16)
Pointer to address 0004 stored at address 001C
Pointer to a pointer in 0024
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
04
00
00
00
1C
00
00
00
5F
01
00
00

## Slide 18: Addresses and Pointers
Address is a location in memory
Pointer is a data object that contains an address
Address 0004 stores the value 351 (or 15F16)
Pointer to address 0004 stored at address 001C
Pointer to a pointer in 0024
Address 0014 stores the value 12
  Is it a pointer?
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
04
00
00
00
1C
00
00
00
5F
01
00
00
0C
00
00
00

## Slide 19: Data Representations
Sizes of objects (in bytes)
  Java Data Type C Data Type Typical 32-bit x86-64
    boolean bool 1 1
    byte char 1 1
    char 2 2
    short short int 2 2
    int int 4 4
    float float 4 4
    long int 4 8
    double double 8 8
    long long long 8 8
    long double 8 16
    (reference) pointer * 4 8

## Slide 20: Byte Ordering
How should bytes within multi-byte word be ordered in memory?
  Peanut butter or chocolate first?
Conventions!
  Big-endian, Little-endian
  Based on Guliver stories, tribes cut eggs on different sides (big, little)

## Slide 21: Byte Ordering Example
Big-Endian (PPC, Internet)
  Least significant byte has highest address
Little-Endian (x86)
  Least significant byte has lowest address
Example
  Variable has 4-byte representation 0x01234567
  Address of variable is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian

## Slide 22: Byte Ordering Example
Big-Endian (PPC, Internet)
  Least significant byte has highest address
Little-Endian (x86)
  Least significant byte has lowest address
Example
  Variable has 4-byte representation 0x01234567
  Address of variable is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67

## Slide 23: Byte Ordering Example
Big-Endian (PPC, Sun, Internet)
  Least significant byte has highest address
Little-Endian (x86)
  Least significant byte has lowest address
Example
  Variable has 4-byte representation 0x01234567
  Address of variable is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 24: Reading Byte-Reversed Listings
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example instruction in memory
  add value 0x12ab to register ‘ebx’ (a special location in CPU’s memory)
Address Instruction Code Assembly Rendition
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx

## Slide 25: Reading Byte-Reversed Listings
Disassembly
  Text representation of binary machine code
  Generated by program that reads the machine code
Example instruction in memory
  add value 0x12ab to register ‘ebx’ (a special location in CPU’s memory)
Address Instruction Code Assembly Rendition
8048366: 81 c3 ab 12 00 00 add $0x12ab,%ebx
Deciphering numbers
  Value: 0x12ab
  Pad to 32 bits: 0x000012ab
  Split into bytes: 00 00 12 ab
  Reverse (little-endian): ab 12 00 00

## Slide 26: Addresses and Pointers in C
Pointer declarations use *
  int * ptr; int x, y; ptr = &x;
  Declares a variable ptr that is a pointer to a data item that is an integer
  Declares integer values named x and y
  Assigns ptr to point to the address where x is stored
We can do arithmetic on pointers
  ptr = ptr + 1; // really adds 4 (because an integer uses 4 bytes)
  Changes the value of the pointer so that it now points to the next data item in memory (that may be y, may not – dangerous!)
To use the value pointed to by a pointer we use de-reference
  y = *ptr + 1; is the same as y = x + 1;
  But, if ptr = &y then y = *ptr + 1; is the same as y = y + 1;
  *ptr is the value stored at the location to which the pointer ptr is pointing
& = ‘address of value’
* = ‘value at address’ or ‘de-reference’
*(&x) is equivalent to x

## Slide 27: Arrays
Arrays represent adjacent locations in memory storing the same type of data object
  E.g., int big_array[128]; allocated 512 adjacent locations in memory starting at 0x00ff0000
Pointers to arrays point to a certain type of object
  E.g., int * array_ptr; array_ptr = big_array; array_ptr = &big_array[0]; array_ptr = &big_array[3]; array_ptr = &big_array[0] + 3; array_ptr = big_array + 3; *array_ptr = *array_ptr + 1; array_ptr = &big_array[130];
  In general: &big_array[i] is the same as (big_array + i)
    which implicitly computes: &bigarray[0] + i*sizeof(bigarray[0]);

## Slide 28: Arrays
Arrays represent adjacent locations in memory storing the same type of data object
  E.g., int big_array[128]; allocated 512 adjacent locations in memory starting at 0x00ff0000
Pointers to arrays point to a certain type of object
  E.g., int * array_ptr; array_ptr = big_array; 0x00ff0000 array_ptr = &big_array[0]; 0x00ff0000 array_ptr = &big_array[3]; 0x00ff000c array_ptr = &big_array[0] + 3; 0x00ff000c (adds 3 * size of int) array_ptr = big_array + 3; 0x00ff000c (adds 3 * size of int) *array_ptr = *array_ptr + 1; 0x00ff000c (but big_array[3] is incremented) array_ptr = &big_array[130]; 0x00ff0208 (out of bounds, C doesn’t check)
  In general: &big_array[i] is the same as (big_array + i)
    which implicitly computes: &bigarray[0] + i*sizeof(bigarray[0]);

## Slide 29: General rules for C (assignments)
Left-hand-side = right-hand-side
  LHS must evaluate to a memory LOCATION
  RHS must evaluate to a VALUE (could be an address)
E.g., x at location 0x04, y at 0x18
  int x, y; x = y; // get value at y and put it in x
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
00
00
00
24
3C
D0
27
00

## Slide 30: General rules for C (assignments)
Left-hand-side = right-hand-side
  LHS must evaluate to a memory LOCATION
  RHS must evaluate to a VALUE (could be an address)
E.g., x at location 0x04, y at 0x18
  int x, y; x = y; // get value at y and put it in x
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
3C
D0
27
00
3C
D0
27
00

## Slide 31: General rules for C (assignments)
Left-hand-side = right-hand-side
  LHS must evaluate to a memory LOCATION
  RHS must evaluate to a VALUE (could be an address)
E.g., x at location 0x04, y at 0x18
  int x, y; x = y; // get value at y and put it in x
  int * x; int y; x = &y + 12; // get address of y add 12
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
3C
D0
27
00
00
00
00
24

## Slide 32: General rules for C (assignments)
Left-hand-side = right-hand-side
  LHS must evaluate to a memory LOCATION
  RHS must evaluate to a VALUE (could be an address)
E.g., x at location 0x04, y at 0x18
  int x, y; x = y; // get value at y and put it in x
  int * x; int y; x = &y + 3; // get address of y add 12
  int * x; int y; *x = y; // value of y to location x points
0000
0004
0008
000C
0010
0014
0018
001C
0020
0024
00
00
00
24
3C
D0
27
00
3C
D0
27
00

## Slide 33: Examining Data Representations
Code to print byte representation of data
  Casting pointer to unsigned char * creates byte array
typedef unsigned char * pointer;
void show_bytes(pointer start, int len)
{
int i;
for (i = 0; i < len; i++)
printf("0x%p\t0x%.2x\n", start+i, start[i]);
printf("\n");
}
Some printf directives:
  %p: Print pointer
  %x: Print hexadecimal
  “\n”: New line
void show_int (int x)
{
show_bytes( (pointer) &x, sizeof(int));
}

## Slide 34: show_bytes Execution Example
int a = 12345; // represented as 0x00003039
printf("int a = 12345;\n");
show_int(a); // show_bytes((pointer) &a, sizeof(int));
Result (Linux):
int a = 12345;
0x11ffffcb8 0x39
0x11ffffcb9 0x30
0x11ffffcba 0x00
0x11ffffcbb 0x00

## Slide 35: Representing Integers
int A = 12345;
int B = -12345;
long int C = 12345;
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 A
30
39
00
00
Sun A
C7
CF
FF
FF
IA32, x86-64 B
CF
C7
FF
FF
Sun B
Two’s complement representation for negative integers (covered later)
00
00
00
00
39
30
00
00
X86-64 C
30
39
00
00
Sun C
39
30
00
00
IA32 C

## Slide 36: Representing Integers
int A = 12345;
int B = -12345;
long int C = 12345;
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 A
30
39
00
00
Sun A
C7
CF
FF
FF
IA32, x86-64 B
CF
C7
FF
FF
Sun B
Two’s complement representation for negative integers (covered later)
00
00
00
00
39
30
00
00
X86-64 C
30
39
00
00
Sun C
39
30
00
00
IA32 C

## Slide 37: Representing Integers
int A = 12345;
int B = -12345;
long int C = 12345;
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 A
30
39
00
00
Sun A
C7
CF
FF
FF
IA32, x86-64 B
CF
C7
FF
FF
Sun B
Two’s complement representation for negative integers (covered later)
00
00
00
00
39
30
00
00
X86-64 C
30
39
00
00
Sun C
39
30
00
00
IA32 C

## Slide 38: Representing Integers
int A = 12345;
int B = -12345;
long int C = 12345;
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 A
30
39
00
00
Sun A
C7
CF
FF
FF
IA32, x86-64 B
CF
C7
FF
FF
Sun B
Two’s complement representation for negative integers (covered later)
00
00
00
00
39
30
00
00
X86-64 C
30
39
00
00
Sun C
39
30
00
00
IA32 C

## Slide 39: Representing Integers
int A = 12345;
int B = -12345;
long int C = 12345;
Decimal: 12345
Binary: 0011 0000 0011 1001
Hex: 3 0 3 9
39
30
00
00
IA32, x86-64 A
30
39
00
00
Sun A
C7
CF
FF
FF
IA32, x86-64 B
CF
C7
FF
FF
Sun B
Two’s complement representation for negative integers (covered later)
00
00
00
00
39
30
00
00
X86-64 C
30
39
00
00
Sun C
39
30
00
00
IA32 C

## Slide 40: Representing Pointers
int B = -12345;
int *P = &B;
FF
7F
00
00
0C
89
EC
FF
x86-64 P
Different compilers & machines assign different locations to objects
FB
2C
EF
FF
Sun P
FF
BF
D4
F8
IA32 P

## Slide 41: Representing strings
A C-style string is represented by an array of bytes.
  Elements are one-byte ASCII codes for each character.
  A 0 value marks the end of the array.
32 | space |  | 48 | 0 |  | 64 | @ |  | 80 | P |  | 96 | ` |  | 112 | p
33 | ! |  | 49 | 1 |  | 65 | A |  | 81 | Q |  | 97 | a |  | 113 | q
34 | ” |  | 50 | 2 |  | 66 | B |  | 82 | R |  | 98 | b |  | 114 | r
35 | # |  | 51 | 3 |  | 67 | C |  | 83 | S |  | 99 | c |  | 115 | s
36 | $ |  | 52 | 4 |  | 68 | D |  | 84 | T |  | 100 | d |  | 116 | t
37 | % |  | 53 | 5 |  | 69 | E |  | 85 | U |  | 101 | e |  | 117 | u
38 | & |  | 54 | 6 |  | 70 | F |  | 86 | V |  | 102 | f |  | 118 | v
39 | ’ |  | 55 | 7 |  | 71 | G |  | 87 | W |  | 103 | g |  | 119 | w
40 | ( |  | 56 | 8 |  | 72 | H |  | 88 | X |  | 104 | h |  | 120 | x
41 | ) |  | 57 | 9 |  | 73 | I |  | 89 | Y |  | 105 | I |  | 121 | y
42 | * |  | 58 | : |  | 74 | J |  | 90 | Z |  | 106 | j |  | 122 | z
43 | + |  | 59 | ; |  | 75 | K |  | 91 | [ |  | 107 | k |  | 123 | {
44 | , |  | 60 | < |  | 76 | L |  | 92 | \ |  | 108 | l |  | 124 | ¦
45 | - |  | 61 | = |  | 77 | M |  | 93 | ] |  | 109 | m |  | 125 | }
46 | . |  | 62 | > |  | 78 | N |  | 94 | ^ |  | 110 | n |  | 126 | ~
47 | / |  | 63 | ? |  | 79 | O |  | 95 | _ |  | 111 | o |  | 127 | del

## Slide 42: Null-terminated Strings
For example, “Harry Potter” can be stored as a 13-byte array.
Why do we put a a 0, or null, at the end of the string?
Computing string length?
72 | 97 | 114 | 114 | 121 | 32 | 80 | 111 | 116 | 116 | 101 | 114 | 0
H | a | r | r | y |  | P | o | t | t | e | r | \0

## Slide 43: Compatibility
char S[6] = "12345";
Byte ordering not an issue
Unicode characters – up to 4 bytes/character
  ASCII codes still work (leading 0 bit) but can support the many characters in all languages in the world
  Java and C have libraries for Unicode (Java commonly uses 2 bytes/char)
Linux/Alpha S
Sun S
33
34
31
32
35
00
33
34
31
32
35
00

## Slide 44: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
  AND: A&B = 1 when both A is 1 and B is 1
  OR: A|B = 1 when either A is 1 or B is 1
  XOR: A^B = 1 when either A is 1 or B is 1, but not both
  NOT: ~A = 1 when A is 0 and vice-versa
  DeMorgan’s Law: ~(A | B) = ~A & ~B

## Slide 45: General Boolean Algebras
Operate on bit vectors
  Operations applied bitwise
All of the properties of Boolean algebra apply
How does this relate to set operations?
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010
01010101
^ 01010101
00111100

## Slide 46: Representing & Manipulating Sets
Representation
  Width w bit vector represents subsets of {0, …, w–1}
  aj = 1 if j  A
    01101001 { 0, 3, 5, 6 }
    76543210
    01010101 { 0, 2, 4, 6 }
    76543210
Operations
  & Intersection 01000001 { 0, 6 }
  | Union 01111101 { 0, 2, 3, 4, 5, 6 }
  ^ Symmetric difference 00111100 { 2, 3, 4, 5 }
  ~ Complement 10101010 { 1, 3, 5, 7 }

## Slide 47: Bit-Level Operations in C
Operations &, |, ^, ~ are available in C
  Apply to any “integral” data type
    long, int, short, char, unsigned
  View arguments as bit vectors
  Arguments applied bit-wise
Examples (char data type)
  ~0x41 --> 0xBE
    ~010000012 --> 101111102
  ~0x00 --> 0xFF
    ~000000002 --> 111111112
  0x69 & 0x55 --> 0x41
    011010012 & 010101012 --> 010000012
  0x69 | 0x55 --> 0x7D
    011010012 | 010101012 --> 011111012

## Slide 48: Contrast: Logic Operations in C
Contrast to logical operators
  &&, ||, !
    View 0 as “False”
    Anything nonzero as “True”
    Always return 0 or 1
    Early termination
Examples (char data type)
  !0x41 --> 0x00
  !0x00 --> 0x01
  !!0x41 --> 0x01
  0x69 && 0x55 --> 0x01
  0x69 || 0x55 --> 0x01
  p && *p++ (avoids null pointer access, null pointer = 0x00000000 )