## Slide 1: Instruction Set Architectures
ISAs
Brief history of processors and architectures
C, assembly, machine code
Assembly basics: registers, operands, move instructions

## Slide 2: What should the HW/SW interface contain?

## Slide 3: The General ISA
PC
...
Registers
Instructions
Memory
Data
CPU

## Slide 4: General ISA Design Decisions
Instructions
  What instructions are available? What do they do?
  How are then encoded?
Registers
  How many registers are there?
  How wide are they?
Memory
  How do you specify a memory location?

## Slide 5: HW/SW Interface: Code / Compile / Run Times
Hardware
User Program in C
Assembler
C
Compiler
.exe File
Code Time
Compile Time
Run Time
What makes programs run fast?

## Slide 6: Executing Programs Fast!
The time required to execute a program depends on:
  The program (as written in C, for instance)
  The compiler: what set of assembler instructions it translates the C program into
  The ISA: what set of instructions it made available to the compiler
  The hardware implementation: how much time it takes to execute an instruction
There is a complicated interaction among these

## Slide 7: Intel x86 Processors
Totally dominate computer market
Evolutionary design
  Backwards compatible up until 8086, introduced in 1978
  Added more features as time goes on
Complex instruction set computer (CISC)
  Many different instructions with many different formats
    But, only small subset encountered with Linux programs
  Hard to match performance of Reduced Instruction Set Computers (RISC)
  But, Intel has done just that!

## Slide 8: Intel x86 Evolution: Milestones
Name Date Transistors MHz
8086 1978 29K 5-10
  First 16-bit processor. Basis for IBM PC & DOS
  1MB address space
386 1985 275K 16-33
  First 32 bit processor , referred to as IA32
  Added “flat addressing”
  Capable of running Unix
  32-bit Linux/gcc uses no instructions introduced in later models
Pentium 4F 2005 230M 2800-3800
  First 64-bit processor
  Meanwhile, Pentium 4s (Netburst arch.) phased out in favor of “Core” line

## Slide 9: Intel x86 Processors, contd.
Machine Evolution
  486 1989 1.9M
  Pentium 1993 3.1M
  Pentium/MMX 1997 4.5M
  PentiumPro 1995 6.5M
  Pentium III 1999 8.2M
  Pentium 4 2001 42M
  Core 2 Duo 2006 291M
Added Features
  Instructions to support multimedia operations
    Parallel operations on 1, 2, and 4-byte data, both integer & FP
  Instructions to enable more efficient conditional operations
Linux/GCC Evolution
  Very limited impact on performance --- mostly came from HW.

## Slide 10: x86 Clones: Advanced Micro Devices (AMD)
Historically
  AMD has followed just behind Intel
  A little bit slower, a lot cheaper
Then
  Recruited top circuit designers from Digital Equipment and other downward trending companies
  Built Opteron: tough competitor to Pentium 4
  Developed x86-64, their own extension to 64 bits
Recently
  Intel much quicker with dual core design
  Intel currently far ahead in performance
  em64t backwards compatible to x86-64

## Slide 11: Intel’s 64-Bit
Intel Attempted Radical Shift from IA32 to IA64
  Totally different architecture (Itanium)
  Executes IA32 code only as legacy
  Performance disappointing
AMD Stepped in with Evolutionary Solution
  x86-64 (now called “AMD64”)
Intel Felt Obligated to Focus on IA64
  Hard to admit mistake or that AMD is better
2004: Intel Announces EM64T extension to IA32
  Extended Memory 64-bit Technology
  Almost identical to x86-64!
Meanwhile: EM64t well introduced, however, still often not used by OS, programs

## Slide 12: Our Coverage in 351
IA32
  The traditional x86
x86-64/EM64T
  The emerging standard – we’ll just touch on its major additions

## Slide 13: Definitions
Architecture: (also instruction set architecture or ISA) The parts of a processor design that one needs to understand to write assembly code (“what is directly visible to SW”)
Microarchitecture: Implementation of the architecture
Architecture examples: instruction set specification, registers
Microarchitecture examples: cache sizes and core frequency
Example ISAs (Intel): x86, IA-32, IPF

## Slide 14: Assembly Programmer’s View
CPU
Programmer-Visible State
  PC: Program counter
    Address of next instruction
    Called “EIP” (IA32) or “RIP” (x86-64)
  Register file
    Heavily used program data
  Condition codes
    Store status information about most recent arithmetic operation
    Used for conditional branching
PC
Registers
Memory
Object Code
Program Data
OS Data
Addresses
Data
Instructions
Stack
Condition
Codes
  Memory
    Byte addressable array
    Code, user data, (some) OS data
    Includes stack used to support procedures (we’ll come back to that)

## Slide 15: Turning C into Object Code
text
text
binary
binary
Compiler (gcc -S)
Assembler (gcc or as)
Linker (gcc or ld)
C program (p1.c p2.c)
Asm program (p1.s p2.s)
Object program (p1.o p2.o)
Executable program (p)
Static libraries (.a)
  Code in files p1.c p2.c
  Compile with command: gcc -O p1.c p2.c -o p
    Use optimizations (-O)
    Put resulting binary in file p

## Slide 16: Compiling Into Assembly
C Code
int sum(int x, int y)
{
int t = x+y;
return t;
}
Generated IA32 Assembly
sum:
pushl %ebp
movl %esp,%ebp
movl 12(%ebp),%eax
addl 8(%ebp),%eax
movl %ebp,%esp
popl %ebp
ret
Obtain with command
  gcc -O -S code.c
Produces file code.s
Some compilers use single instruction “leave”

## Slide 17: Three Kinds of Instructions
Perform arithmetic function on register or memory data
Transfer data between memory and register
  Load data from memory into register
  Store register data into memory
Transfer control (control flow)
  Unconditional jumps to/from procedures
  Conditional branches

## Slide 18: Assembly Characteristics: Data Types
“Integer” data of 1, 2, or 4 bytes
  Data values
  Addresses (untyped pointers)
Floating point data of 4, 8, or 10 bytes
No aggregate types such as arrays or structures
  Just contiguously allocated bytes in memory

## Slide 19: Object Code
Code for sum
0x401040 <sum>: 0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x89
0xec
0x5d
0xc3
Assembler
  Translates .s into .o
  Binary encoding of each instruction
  Nearly-complete image of executable code
  Missing linkages between code in different files
Linker
  Resolves references between files
  Combines with static run-time libraries
    E.g., code for malloc, printf
  Some libraries are dynamically linked
    Linking occurs when program begins execution
  Total of 13 bytes
  Each instruction 1, 2, or 3 bytes
  Starts at address 0x401040

## Slide 20: Machine Instruction Example
C Code
  Add two signed integers
Assembly
  Add 2 4-byte integers
    “Long” words in GCC parlance
    Same instruction whether signed or unsigned
  Operands:
    x: Register %eax
    y: Memory M[%ebp+8]
    t: Register %eax
      Return function value in %eax
Object Code
  3-byte instruction
  Stored at address 0x401046
int t = x+y;
addl 8(%ebp),%eax
0x401046: 03 45 08
Similar to expression:
x += y
More precisely:
int eax;
int *ebp;
eax += ebp[2]

## Slide 21: Disassembling Object Code
Disassembled
00401040 <_sum>:
0: 55 push %ebp
1: 89 e5 mov %esp,%ebp
3: 8b 45 0c mov 0xc(%ebp),%eax
6: 03 45 08 add 0x8(%ebp),%eax
9: 89 ec mov %ebp,%esp
b: 5d pop %ebp
c: c3 ret
d: 8d 76 00 lea 0x0(%esi),%esi
Disassembler
  objdump -d p
  Useful tool for examining object code
  Analyzes bit pattern of series of instructions
  Produces approximate rendition of assembly code
  Can be run on either a.out (complete executable) or .o file

## Slide 22: Alternate Disassembly
Disassembled
0x401040 <sum>: push %ebp
0x401041 <sum+1>: mov %esp,%ebp
0x401043 <sum+3>: mov 0xc(%ebp),%eax
0x401046 <sum+6>: add 0x8(%ebp),%eax
0x401049 <sum+9>: mov %ebp,%esp
0x40104b <sum+11>: pop %ebp
0x40104c <sum+12>: ret
0x40104d <sum+13>: lea 0x0(%esi),%esi
Within gdb Debugger
  gdb p
  disassemble sum
  Disassemble procedure
  x/13b sum
  Examine the 13 bytes starting at sum
Object
0x401040:
0x55
0x89
0xe5
0x8b
0x45
0x0c
0x03
0x45
0x08
0x89
0xec
0x5d
0xc3

## Slide 23: What Can be Disassembled?
Anything that can be interpreted as executable code
Disassembler examines bytes and reconstructs assembly source
% objdump -d WINWORD.EXE
WINWORD.EXE: file format pei-i386
No symbols in "WINWORD.EXE".
Disassembly of section .text:
30001000 <.text>:
30001000: 55 push %ebp
30001001: 8b ec mov %esp,%ebp
30001003: 6a ff push $0xffffffff
30001005: 68 90 10 00 30 push $0x30001090
3000100a: 68 91 dc 4c 30 push $0x304cdc91

## Slide 24: Integer Registers (IA32)
%eax
%ecx
%edx
%ebx
%esi
%edi
%esp
%ebp
%ax
%cx
%dx
%bx
%si
%di
%sp
%bp
%ah
%ch
%dh
%bh
%al
%cl
%dl
%bl
16-bit virtual registers
(backwards compatibility)
general purpose
accumulate
counter
data
base
source
index
destination
index
stack
pointer
base
pointer
Origin
(mostly obsolete)