## Slide 1: CSE 451: Operating Systems Winter 2022 Module 17 Redundant Arrays of Inexpensive Disks (RAID)
Gary Kimura
Notes: 1x day
1

## Slide 2: The challenge
Disk transfer rates are improving, but much less fast than CPU performance
We can use multiple disks to improve performance
  by striping files across multiple disks (placing parts of each file on a different disk), we can use parallel I/O to improve access time
Striping reduces reliability
  100 disks have 1/100th the MTBF (mean time between failures) of one disk
So, we need striping for performance, but we need something to help with reliability / availability
To improve reliability, we can add redundant data to the disks, in addition to striping

## Slide 3: RAID
A RAID is a Redundant Array of Inexpensive Disks
Disks are small (physically) and cheap, so it’s easy to put lots of disks (10s to 100s) in one box for increased storage, performance, and availability
Data plus some redundant information is striped across the disks in some way
How striping is done is key to performance and reliability

## Slide 4: Some RAID tradeoffs
Granularity
  fine-grained: stripe each file over all disks
    high throughput for the file
    limits transfer to 1 file at a time
  coarse-grained: stripe each file over only a few disks
    limits throughput for 1 file
    allows concurrent access to multiple files
Redundancy
  uniformly distribute redundancy information on disks
    avoids load-balancing problems
  concentrate redundancy information on a small number of disks
    partition the disks into data disks and redundancy disks

## Slide 5: RAID Level 0
RAID Level 0 is a non-redundant disk array
Files are striped across disks, no redundant info
High read throughput
Best write throughput (no redundant info to write)
Any disk failure results in data loss; sometimes a file, sometimes the entire volume

## Slide 6: RAID Level 1
RAID Level 1 is mirrored disks
Files are striped across (half) the disks
Data is written to multiple (two) places – data disks and mirror disks
On failure, just use the surviving disk(s)
Factor of N (2x) space expansion
data disks
mirror copies

## Slide 7: RAID Levels 2, 3, and 4
RAID levels 2, 3, and 4 use ECC (error correcting code) or parity disks
  E.g., each byte on the parity disk is a parity function of the corresponding bytes on all the other disks
A read accesses all the data disks
A write accesses all the data disks plus the parity disk
On disk failure, read the remaining disks plus the parity disk to compute the missing data
data disks
parity disk

## Slide 8: Refresher: What’s parity?
To each byte, add a bit set so that the total number of 1’s is even
Any single missing bit can be reconstructed
(Why does memory parity not work quite this way?)
1
0
1
1
0
1
1
0
1

## Slide 9: RAID Level 5
RAID Level 5 uses block interleaved distributed parity
Like parity scheme, but distribute the parity info (as well as data) over all disks
  for each block, one disk holds the parity, and the other disks hold the data
Significantly better performance
  parity disk is not a hot spot
0
1
2
3
PO
5
6
7
P1
4
10
11
P2
8
9
data & parity drives
File Block
Numbers

## Slide 10: Management
Multiple spindles complicates things
  Visible to: Apps? File system?
  Allocation of space (per user on a “file server”)
  SANs
  Differing disk sizes
Partitions!
  Logical division of spindle into blocks
  Assemble volumes from partitions

## Slide 11: OS and Hardware Layering
Who needs to know?
  FS: probably not
Operating System
File System
Fault Tolerance
Volume Manager
Device Driver
Disk 0
Disk 1
Disk 2
Disk Controller

## Slide 12: OS and Hardware Layering
Why put FT into hardware?
  Speed
  Simplicity of OS
Why not?
  Fixes
  CvI data
Operating System
File System
Volume Manager
Device Driver
Disk 0
Disk 1
Disk 2
Disk Controller w/ FT

## Slide 13: One tiny problem with RAID and multiple spindles…
How do you boot?
  ROM on motherboard doesn’t have a lot of room for logic
  Boot zone on disk doesn’t have a lot of room for logic (and needs to be replicated, striped, etc.)
  Put partition info into “well-known place”
  Put RAID info into “well-known place”
  Still… too complicated
“Real systems”…
  Don’t boot from multi-partition volumes
  Boot from RAID 0, at most RAID 1 (simple failover)