## Slide 1: Stereo
CSE 455
Ali Farhadi
Several slides from Larry Zitnick and Steve Seitz

## Slide 3
Why do we perceive depth?

## Slide 4: What do humans use as depth cues?
Convergence
When watching an object close to us, our eyes point slightly inward. This difference in the direction of the eyes is called convergence. This depth cue is effective only on short distances (less than 10 meters).
Marko Teittinen http://www.hitl.washington.edu/scivw/EVE/III.A.1.c.DepthCues.html
Motion
Focus
Binocular Parallax
As our eyes see the world from slightly different locations, the images sensed by the eyes are slightly different. This difference in the sensed images is called binocular parallax. Human visual system is very sensitive to these differences, and binocular parallax is the most important depth cue for medium viewing distances. The sense of depth can be achieved using binocular parallax even if all other depth cues are removed.
Monocular Movement Parallax
If we close one of our eyes, we can perceive depth by moving our head. This happens because human visual system can extract depth information in two similar images sensed after each other, in the same way it can combine two images from different eyes.
Accommodation
Accommodation is the tension of the muscle that changes the focal length of the lens of eye. Thus it brings into focus objects at different distances. This depth cue is quite weak, and it is effective only at short viewing distances (less than 2 meters) and with other cues.

## Slide 5: What do humans use as depth cues?
Shades and Shadows
When we know the location of a light source and see objects casting shadows on other objects, we learn that the object shadowing the other is closer to the light source. As most illumination comes downward we tend to resolve ambiguities using this information. The three dimensional looking computer user interfaces are a nice example on this. Also, bright objects seem to be closer to the observer than dark ones.
Marko Teittinen http://www.hitl.washington.edu/scivw/EVE/III.A.1.c.DepthCues.html
Image cues
Retinal Image Size
When the real size of the object is known, our brain compares the sensed size of the object to this real size, and thus acquires information about the distance of the object.
Linear Perspective
When looking down a straight level road we see the parallel sides of the road meet in the horizon. This effect is often visible in photos and it is an important depth cue. It is called linear perspective.
Texture Gradient
The closer we are to an object the more detail we can see of its surface texture. So objects with smooth textures are usually interpreted being farther away. This is especially true if the surface texture spans all the distance from near to far.
Overlapping
When objects block each other out of our sight, we know that the object that blocks the other one is closer to us. The object whose outline pattern looks more continuous is felt to lie closer.
Aerial Haze
The mountains in the horizon look always slightly bluish or hazy. The reason for this are small water and dust particles in the air between the eye and the mountains. The farther the mountains, the hazier they look.
Jonathan Chiu

## Slide 7: Amount of horizontal movement is …
…inversely proportional to the distance from the camera

## Slide 8: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
f
x
x’
Baseline B
z
C
C’
X
f
X
x
x'

## Slide 9: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 10: Depth from Stereo
Goal: recover depth by finding image coordinate x’ that corresponds to x
Sub-Problems
  Calibration: How do we recover the relation of the cameras (if not already known)?
  Correspondence: How do we search for the matching point x’?
X
x
x'

## Slide 11: Correspondence Problem
We have two images taken from cameras with different intrinsic and extrinsic parameters
How do we match a point in the first image to a point in the second? How can we constrain our search?
x
?

## Slide 12: Key idea: Epipolar constraint
Potential matches for x have to lie on the corresponding line l’.
Potential matches for x’ have to lie on the corresponding line l.
x
x’
X
x’
X
x’
X

## Slide 13: Epipolar geometry: notation
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers
X
x
x’

## Slide 14: Epipolar geometry: notation
Epipolar Lines - intersections of epipolar plane with image planes (always come in corresponding pairs)
X
x
x’
Epipolar Plane – plane containing baseline (1D family)
Epipoles
= intersections of baseline with image planes
= projections of the other camera center
Baseline – line connecting the two camera centers

## Slide 15: Example: Converging cameras

## Slide 16: Example: Motion parallel to image plane

## Slide 17: Example: Forward motion
What would the epipolar lines look like if the camera moves directly forward?

## Slide 18: Example: Motion perpendicular to image plane

## Slide 19: Example: Motion perpendicular to image plane
Points move along lines radiating from the epipole: “focus of expansion”
Epipole is the principal point

## Slide 20: Example: Forward motion
e
e’
Epipole has same coordinates in both images.
Points move along lines radiating from “Focus of expansion”

## Slide 21: Epipolar constraint
If we observe a point x in one image, where can the corresponding point x’ be in the other image?
x
x’
X

## Slide 22: Epipolar constraint
Potential matches for x have to lie on the corresponding
epipolar line l’.
Potential matches for x’ have to lie on the corresponding
epipolar line l.
x
x’
X
x’
X
x’
X

## Slide 23: Epipolar constraint example

## Slide 24: Epipolar constraint: Calibrated case
X
x
x’
Assume that the intrinsic and extrinsic parameters of the cameras are known
We can multiply the projection matrix of each camera (and the image points) by the inverse of the calibration matrix to get normalized image coordinates
We can also set the global coordinate system to the coordinate system of the first camera. Then the projection matrices of the two cameras can be written as [I | 0] and [R | t]

## Slide 25: Epipolar constraint: Calibrated case
X
x
x’ = Rx+t
R
t
The vectors Rx, t, and x’ are coplanar
= (x,1)T
Notes: X’ is X in the second camera’s coordinate system
We can identify the non-homogeneous 3D vectors X and X’ with the homogeneous coordinate vectors x and x’ of the projections of the two points into the two respective images

## Slide 26: Epipolar constraint: Calibrated case
Essential Matrix
(Longuet-Higgins, 1981)
X
x
x’
The vectors Rx, t, and x’ are coplanar

## Slide 27: Epipolar constraint: Calibrated case
X
x
x’
E x is the epipolar line associated with x (l' = E x)
ETx' is the epipolar line associated with x' (l = ETx')
E e = 0 and ETe' = 0
E is singular (rank two)
E has five degrees of freedom

## Slide 28: Epipolar constraint: Uncalibrated case
The calibration matrices K and K’ of the two cameras are unknown
We can write the epipolar constraint in terms of unknown normalized coordinates:
X
x
x’

## Slide 29: Epipolar constraint: Uncalibrated case
X
x
x’
Fundamental Matrix
(Faugeras and Luong, 1992)

## Slide 30: Epipolar constraint: Uncalibrated case
F x is the epipolar line associated with x (l' = F x)
FTx' is the epipolar line associated with x' (l' = FTx')
F e = 0 and FTe' = 0
F is singular (rank two)
F has seven degrees of freedom
X
x
x’

## Slide 31: The eight-point algorithm
Minimize:
under the constraint ||F||2=1
Smallest eigenvalue of ATA
A

## Slide 32: The eight-point algorithm
Meaning of error sum of squared algebraic distances between points x’i and epipolar lines F xi (or points xi and epipolar lines FTx’i)
Nonlinear approach: minimize sum of squared geometric distances

## Slide 33: Problem with eight-point algorithm

## Slide 34: Problem with eight-point algorithm
Poor numerical conditioning
Can be fixed by rescaling the data

## Slide 35: The normalized eight-point algorithm
Center the image data at the origin, and scale it so the mean squared distance between the origin and the data points is 2 pixels
Use the eight-point algorithm to compute F from the normalized points
Enforce the rank-2 constraint (for example, take SVD of F and throw out the smallest singular value)
Transform fundamental matrix back to original units: if T and T’ are the normalizing transformations in the two images, then the fundamental matrix in original coordinates is T’T F T
(Hartley, 1995)

## Slide 36: Comparison of estimation algorithms
 | 8-point | Normalized 8-point | Nonlinear least squares
Av. Dist. 1 | 2.33 pixels | 0.92 pixel | 0.86 pixel
Av. Dist. 2 | 2.18 pixels | 0.85 pixel | 0.80 pixel

## Slide 37: Moving on to stereo…
Fuse a calibrated binocular stereo pair to produce a depth image
image 1
image 2
Dense depth map
Many of these slides adapted from Steve Seitz and Lana Lazebnik

## Slide 38: Depth from disparity
f
x’
Baseline B
z
O
O’
X
f
Disparity is inversely proportional to depth.
x

## Slide 39: Basic stereo matching algorithm
If necessary, rectify the two stereo images to transform epipolar lines into scanlines
For each pixel x in the first image
  Find corresponding epipolar scanline in the right image
  Search the scanline and pick the best match x’
  Compute disparity x-x’ and set depth(x) = fB/(x-x’)

## Slide 40: Basic stereo matching algorithm
For each pixel in the first image
  Find corresponding epipolar line in the right image
  Search along epipolar line and pick the best match
  Triangulate the matches to get depth information
Simplest case: epipolar lines are scanlines
  When does this happen?

## Slide 41: Simplest Case: Parallel images
Epipolar constraint:
R = I t = (T, 0, 0)
The y-coordinates of corresponding points are the same
t
x
x’

## Slide 42: Stereo image rectification

## Slide 43: Stereo image rectification
Reproject image planes onto a common plane parallel to the line between camera centers
Pixel motion is horizontal after this transformation
Two homographies (3x3 transform), one for each input image reprojection
C. Loop and Z. Zhang. Computing Rectifying Homographies for Stereo Vision. IEEE Conf. Computer Vision and Pattern Recognition, 1999.

## Slide 44: Example
Unrectified
Rectified

## Slide 45: Correspondence search
Matching cost
disparity
Left
Right
scanline
Slide a window along the right scanline and compare contents of that window with the reference window in the left image
Matching cost: SSD or normalized correlation

## Slide 46: Correspondence search
Left
Right
scanline
SSD

## Slide 47: Correspondence search
Left
Right
scanline
Norm. corr

## Slide 48: Effect of window size
W = 3
W = 20
Smaller window
  + More detail
  More noise
Larger window
  + Smoother disparity maps
  Less detail
  Fails near boundaries
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 49: Failures of correspondence search
Textureless surfaces
Occlusions, repetition
Non-Lambertian surfaces, specularities

## Slide 50: Results with window search
Window-based matching
Ground truth
Data

## Slide 51: How can we improve window-based matching?
So far, matches are independent for each point
What constraints or priors can we add?

## Slide 52: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image

## Slide 53: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views

## Slide 54: Stereo constraints/priors
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Ordering constraint doesn’t hold

## Slide 55: Priors and constraints
Uniqueness
  For any point in one image, there should be at most one matching point in the other image
Ordering
  Corresponding points should be in the same order in both views
Smoothness
  We expect disparity values to change slowly (for the most part)

## Slide 56: Stereo as energy minimization
What defines a good stereo correspondence?
  Match quality
    Want each pixel to find a good match in the other image
  Smoothness
    If two pixels are adjacent, they should (usually) move about the same amount

## Slide 57: Stereo as energy minimization
Better objective function
{
{
match cost
smoothness cost
    Want each pixel to find a good match in the other image
    Adjacent pixels should (usually) move about the same amount

## Slide 58: Stereo as energy minimization
match cost:
smoothness cost:
4-connected neighborhood
8-connected neighborhood
: set of neighboring pixels
SSD distance between windows I(x, y) and J(x, y + d(x,y))
=

## Slide 59: Smoothness cost
“Potts model”
L1 distance

## Slide 60: Dynamic programming
Can minimize this independently per scanline using dynamic programming (DP)
: minimum cost of solution such that d(x,y) = d

## Slide 61: Energy minimization via graph cuts
Labels
(disparities)
d1
d2
d3
edge weight
edge weight

## Slide 62: Energy minimization via graph cuts
d1
d2
d3
Graph Cut
  Delete enough edges so that
    each pixel is connected to exactly one label node
  Cost of a cut: sum of deleted edge weights
  Finding min cost cut equivalent to finding global minimum of energy function

## Slide 63: Stereo as energy minimization
I(x, y)
J(x, y)
y = 141
C(x, y, d); the disparity space image (DSI)
x
d

## Slide 64: Stereo as energy minimization
y = 141
x
d
Simple pixel / window matching: choose the minimum of each column in the DSI independently:

## Slide 65: Matching windows
Similarity Measure | Formula
Sum of Absolute Differences (SAD) | 
Sum of Squared Differences (SSD) | 
Zero-mean SAD | 
Locally scaled SAD | 
Normalized Cross Correlation (NCC) | 
http://siddhantahuja.wordpress.com/category/stereo-vision/
SAD
SSD
NCC
Ground truth
Notes: smaller window: more detail, more noise
bigger window: less noise, more detail

## Slide 66: Before & After
Graph cuts
Ground truth
    For the latest and greatest: http://www.middlebury.edu/stereo/
  Y. Boykov, O. Veksler, and R. Zabih, Fast Approximate Energy Minimization via Graph Cuts, PAMI 2001
Before

## Slide 67: Real-time stereo
Used for robot navigation (and other tasks)
  Several software-based real-time stereo techniques have been developed (most based on simple discrete search)
Nomad robot searches for meteorites in Antartica
  http://www.frc.ri.cmu.edu/projects/meteorobot/index.html

## Slide 68: Why does stereo fail?
Fronto-Parallel Surfaces: Depth is constant within the region of local support

## Slide 69: Why does stereo fail?
Monotonic Ordering - Points along an epipolar scanline appear in the same order in both stereo images
Occlusion – All points are visible in each image

## Slide 70: Why does stereo fail?
Image Brightness Constancy: Assuming Lambertian surfaces, the brightness of corresponding
points in stereo images are the same.

## Slide 71: Why does stereo fail?
Match Uniqueness: For every point in one stereo image, there is at most one corresponding point in the other image.

## Slide 72: Stereo reconstruction pipeline
  Camera calibration errors
  Poor image resolution
  Occlusions
  Violations of brightness constancy (specular reflections)
  Large motions
  Low-contrast image regions
Steps
  Calibrate cameras
  Rectify images
  Compute disparity
  Estimate depth
What will cause errors?

## Slide 73: Choosing the stereo baseline
width of
a pixel
What’s the optimal baseline?
  Too small: large depth error
  Too large: difficult search problem
Large Baseline
Small Baseline
all of these
points project
to the same
pair of pixels

## Slide 74: Multi-view stereo ?

## Slide 75: Beyond two-view stereo
The third view can be used for verification

## Slide 76: Using more than two images
Multi-View Stereo for Community Photo Collections M. Goesele, N. Snavely, B. Curless, H. Hoppe, S. Seitz Proceedings of ICCV 2007,