# Introduction to DSP

Agenda

- Sampling: benefits and drawbacks

- Aliasing

The Nyquist frequency

Avoiding aliasing

- Fundamentals of periodic signal processing

- Digital Filters

Sampling (Pulse Code Modulation)

- The signal is sampled at regular intervals and converted to binary numbers

PCM Features

- Drawbacks

Loss of information/precision

Quantization noise

Might require very expensive equipment (especially for high frequencies)

- Advantages

Fidelity

Ease of Storage

Lossless transport and storage

Phenomenal scalability

Ease of processing

Sampling Strategies

- In the time domain:

Use logarithmic sampling thresholds (minimize relative error)

Differential PCM (DPCM)

Adaptive Differential PCM (ADPCM)

Fuzzy/Neural Predictor-based encoding

Psychoacoustics – encode audio exploiting human sound perception specifics.

- In the frequency domain:

Transform-based encoding. The signal is “teleported” to a space where nonessential features and redundancies appear conspicuous and are easy to eliminate.

Fourier transform

Discrete Cosine transform

MP3!

Aliasing. The Nyquist Frequency

- If the sampling frequency falls below the double of the sampled signal frequency, the result is a false frequency signal – an alias.

- Nyquist Frequency: fN = 2 * fmax

Aliasing (cont’d)

- Similar to the “wagon wheel illusion”

Sometimes, wagon wheels in movies seem to move backwards

The phenomenon also manifests in continuous light!?!?!

- If you want an accurate reproduction of the signal, you need to sample it at least twice as fast as the highest frequency component.

Even if the highest frequency in the original signal is inaudible, and would remain inaudible through analog processing, it will produce audible noise after sampling. Aliasing is a problem specific to DSP.

A quality low-pass filter preceding sampling is required.

- Oversampling is the best solution: use a sampling rate much greater than the Nyquist frequency.

Fourier Decomposition

- Any periodic signal can be viewed as the superposition of an infinite series of sine and cosine signals.

That is any, such as the square wave.

- Formula:

- Applicability – the signal’s coefficients are computed, then some of them are eliminated → compression.

- Conversely, you can build any signal by composing sine waves with various frequencies and intensities.

The concept behind a whole breed of signal generators.

Introduction to Digital Filters

- A filter is a device that selectively changes the characteristics of a signal (shape, amplitude-frequency, phase-frequency)

- Filtering applications:

Noise reduction

Separating mixed modulated signals (DSL, Cable modems, telephony...)

Improve music listening experience (bass boost, loudness etc.)

- Digital filters are algorithms that operate on digitized streams of signals and implement filtering functionality

- Advantages:

“Perfect filters”: characteristics impossible to attain with analog filters.

No thermal/noise/decalibration problems

Easy to build complex, adaptive filters

“Off-line filtering” – you can apply a complex, slow filter and save the filtered data

Scalability – quality is dictated by the word length used

Repeatability – built one, built’em all

Digital Filters (cont’d)

- Disadvantages

Limited speed

New types of noise – quantization and roundoff

Might be hard to design